## Slide 1: PMR Packet Taxonomy: Ultra Ethernet Technical Report
UE Specification v1.0.1 Protocol Formats
Packet Taxonomy Team
Cornelis Networks Engineering

## Slide 2: Ultra Ethernet Overview
Protocol Architecture and Key Characteristics

## Slide 3: UE Protocol Key Characteristics
• High-performance RDMA transport over Ethernet infrastructure
• Layered architecture: Physical, Link, Network, Transport
• Transport sublayers: PDS (Packet Delivery), SES (Semantic), CMS (Congestion), TSS (Security)
• Multiple delivery modes: RUD, ROD, RUDI, UUD
• Congestion control algorithms: NSCC, RCCC, TFC
• Link-layer reliability via LLR (Link Layer Reliable)
• Credit-based flow control via CBFC
• AES-GCM encryption via TSS

## Slide 4: UE Datamodel Coverage Summary
Layer | Sublayer | Format Files | Protocol Files | Total
Transport | PDS | 14 | 16 | 30
Transport | SES | 15 | 12 | 27
Transport | CMS | 7 | 8 | 15
Transport | TSS | 2 | 7 | 9
Link | LLR | 6 | 3 | 9
Link | LLDP | 2 | 1 | 3
Link | CBFC | 2 | 3 | 5
Network | - | 4 | 0 | 4
Physical | - | 1 | 0 | 1
**Total** | - | **53** | **50** | **103**

## Slide 5: Protocol Architecture
UE Layer Diagram and Sublayer Relationships

## Slide 6: UE Protocol Stack (text)
+------------------------------------------------------------------+
| Application / RDMA Verbs |
+------------------------------------------------------------------+
| |
| TRANSPORT LAYER |
| +-------------------------------------------------------------+ |
| | SES (Semantic Sublayer) | |
| | - Request/Response operations | |
| | - RDMA Read/Write, Atomics, Tagged Send | |
| +-------------------------------------------------------------+ |
| | PDS (Packet Delivery Sublayer) | |
| | - Reliable/Unreliable delivery | |
| | - Sequence numbers, ACK/NACK | |
| +-------------------------------------------------------------+ |
| | CMS (Congestion Management Sublayer) | |
| | - NSCC, RCCC, TFC algorithms | |
| +-------------------------------------------------------------+ |
| | TSS (Transport Security Sublayer) | |
| | - AES-GCM encryption | |
| +-------------------------------------------------------------+ |
| |
+------------------------------------------------------------------+
| NETWORK LAYER |
| - IPv4/IPv6 encapsulation |
| - DSCP categories, packet trimming |
+------------------------------------------------------------------+
| LINK LAYER |
| +-------------------------------------------------------------+ |
| | LLR (Link Layer Reliable) | |
| | - Hop-by-hop reliability | |
| +-------------------------------------------------------------+ |
| | CBFC (Credit-Based Flow Control) | |
| | - Per-VC flow control | |
| +-------------------------------------------------------------+ |
+------------------------------------------------------------------+
| PHYSICAL LAYER |
| - 64B/66B encoding, Control Ordered Sets |
+------------------------------------------------------------------+

## Slide 7: PDS Header Building Blocks
Packet Delivery Sublayer Format Definitions

## Slide 8: PDS Wire Formats (14 files)
Type | Format | KSY File | Size | Description
0x01 | RUD Request | rud_rod_request.ksy | 12B | Reliable Unordered Delivery
0x02 | ROD Request | rud_rod_request.ksy | 12B | Reliable Ordered Delivery
0x04 | RUDI Request | rudi_request_response.ksy | 6B | Reliable Unordered Immediate
0x05 | RUDI Response | rudi_request_response.ksy | 6B | RUDI response
0x06 | UUD Request | uud_request.ksy | 6B | Unreliable Unordered Delivery
0x07 | ACK | rud_rod_ack.ksy | 12B | Acknowledgment
0x08 | ACK_CC | ack_cc.ksy | 28B | ACK with CC state
0x09 | ACK_CCX | ack_ccx.ksy | 44B | ACK with extended CC
0x0A | NACK | nack.ksy | 12B | Negative acknowledgment
0x0B | CP | rud_rod_cp.ksy | 12B | Control packet (10 subtypes)
0x0C | NACK_CCX | nack_ccx.ksy | 28B | NACK with extended CC
0x0D | RUD_CC_REQ | rud_rod_request_cc.ksy | 28B | RUD with CC state
0x0E | ROD_CC_REQ | rud_rod_request_cc.ksy | 28B | ROD with CC state
- | Prologue | prologue.ksy | 2B | PDS header prologue
- | Entropy Header | entropy_header.ksy | 4B | ECMP entropy (non-UDP)
- | Default SES | rud_rod_default_ses.ksy | 8B | Default SES response
- | NACK Codes | nack_codes.ksy | - | NACK reason codes enum

## Slide 9: PDS Protocol State Machines (16 files)
Protocol | KSY File | UE Spec Section | Description
PDC Establishment | pdc_establishment.ksy | 3.5.7 | PDC setup handshake
PDC Close | pdc_close.ksy | 3.5.7 | PDC teardown
PDC Initiator | pdc_initiator.ksy | 3.5.7 | Initiator state machine
PDC Target | pdc_target.ksy | 3.5.7 | Target state machine
PDS Manager | pds_manager.ksy | 3.5.7 | PDS management
RUD Delivery | rud_delivery.ksy | 3.5.10.3 | RUD delivery protocol
ROD Delivery | rod_delivery.ksy | 3.5.10.3 | ROD delivery protocol
RUDI Delivery | rudi_delivery.ksy | 3.5.10.9 | RUDI delivery protocol
Loss Detection CACK/SACK | loss_detection_cack_sack.ksy | 3.5.11 | Cumulative/Selective ACK
Loss Detection EV | loss_detection_ev.ksy | 3.5.11 | Early validation
Loss Detection NACK | loss_detection_nack.ksy | 3.5.11 | NACK-based detection
Loss Detection OOO | loss_detection_ooo.ksy | 3.5.11 | Out-of-order detection
Loss Detection Receiver | loss_detection_receiver.ksy | 3.5.11 | Receiver-side detection
Loss Detection RTO | loss_detection_rto.ksy | 3.5.11 | Retransmit timeout
Loss Detection Tail | loss_detection_tail.ksy | 3.5.11 | Tail loss detection
Loss Detection Trimming | loss_detection_trimming.ksy | 3.5.11 | Trimmed packet detection

## Slide 10: SES Header Building Blocks
Semantic Sublayer Format Definitions

## Slide 11: SES Wire Formats (15 files)
next_hdr | Format | KSY File | Size | Description
0x0 | Standard Request SOM=1 | standard_request_som1.ksy | 44B | Start of message
0x1 | Standard Request SOM=0 | standard_request_som0.ksy | 16B | Continuation
0x2 | Optimized Non-Matching | optimized_non_matching.ksy | 32B | Optimized RMA
0x3 | Small Message | small_message.ksy | 32B | Single-packet optimized
0x3 | Small RMA | small_rma.ksy | 32B | Small RMA operations
0x4 | Response | response.ksy | 16B | Standard response
0x5 | Response with Data | response_with_data.ksy | 24B | Data-carrying response
0x6 | Optimized Response | optimized_response_with_data.ksy | 16B | Optimized format
- | Rendezvous Extension | rendezvous_extension.ksy | 32B | Large message protocol
- | Atomic Extension | atomic_extension.ksy | 8B | Atomic operations
- | CAS Extension | cas_extension.ksy | 40B | Compare-and-swap
- | Deferrable Send | deferrable_send_request.ksy | 44B | Deferrable send request
- | Ready to Restart | ready_to_restart.ksy | 44B | RTR response
- | Opcodes | opcodes.ksy | - | SES opcode definitions
- | Next Header Types | next_header_types.ksy | - | Header type enum

## Slide 12: SES Message Sequences (12 files)
Sequence | KSY File | Description
Single Packet Request | single_packet_request.ksy | Single-packet message flow
Multi Packet Request | multi_packet_request.ksy | Multi-packet message flow
Read Standard | read_standard.ksy | Standard RDMA read
Read Large ACK | read_large_ack.ksy | Large read with ACK
Rendezvous Expected | rendezvous_expected.ksy | Rendezvous with posted receive
Rendezvous Unexpected | rendezvous_unexpected.ksy | Rendezvous without posted receive
Deferrable Expected | deferrable_expected.ksy | Deferrable with buffer
Deferrable Unexpected | deferrable_unexpected.ksy | Deferrable without buffer
Deferrable No Buffer | deferrable_no_buffer.ksy | Deferrable RTR flow
Buffered Messages | buffered_messages.ksy | Message buffering
Buffered Headers | buffered_headers.ksy | Header buffering
Backoff Retry | backoff_retry.ksy | Retry with backoff

## Slide 13: CMS Header Building Blocks
Congestion Management Sublayer Format Definitions

## Slide 14: CMS Wire Formats (7 files)
Format | KSY File | Size | Description
ACK CC State NSCC | ack_cc_state_nscc.ksy | 8B | NSCC congestion state
ACK CC State RCCC/TFC | ack_cc_state_rccc_tfc.ksy | 8B | Credit-based CC state
Request CC State | req_cc_state.ksy | 8B | Source CC state
Credit CP Payload | credit_cp_payload.ksy | Var | Credit control packet
Credit Request Payload | credit_request_cp_payload.ksy | Var | Credit request
CC Type | cc_type.ksy | - | CC algorithm type enum
CCX Type | ccx_type.ksy | - | Extended CC type enum

## Slide 15: CMS Protocol State Machines (8 files)
Protocol | KSY File | UE Spec Section | Description
CCC State Machine | ccc_state_machine.ksy | 3.6.6 | Congestion Control Context
NSCC Source | nscc_source.ksy | 3.6.13.3-6 | NSCC source algorithm
NSCC Destination | nscc_destination.ksy | 3.6.13.9 | NSCC destination algorithm
RCCC Source | rccc_source.ksy | 3.6.14.2-4 | RCCC source algorithm
RCCC Destination | rccc_destination.ksy | 3.6.14.6 | RCCC destination algorithm
TFC Source | tfc_source.ksy | 3.6.15 | TFC source algorithm
TFC Destination | tfc_destination.ksy | 3.6.15 | TFC destination algorithm
Multipath Selection | multipath_selection.ksy | 3.6.16 | ECMP path selection

## Slide 16: TSS Header Building Blocks
Transport Security Sublayer Format Definitions

## Slide 17: TSS Wire Formats (2 files)
Format | KSY File | Size | Description
Security Header | security_header.ksy | 12-16B | AES-GCM encryption header
IV Construction | iv_construction.ksy | 12B | Initialization vector

## Slide 18: TSS Protocol State Machines (7 files)
Protocol | KSY File | UE Spec Section | Description
TSS TX Processing | tss_tx_processing.ksy | 3.7 | Transmit encryption
TSS RX Processing | tss_rx_processing.ksy | 3.7 | Receive decryption
Key Rotation | key_rotation.ksy | 3.7 | Key rotation protocol
Join Secure Domain | join_secure_domain.ksy | 3.7 | Domain join protocol
KDF Direct | kdf_direct.ksy | 3.7 | Direct key derivation
KDF Client Server | kdf_client_server.ksy | 3.7 | Client-server KDF
KDF Cluster | kdf_cluster.ksy | 3.7 | Cluster KDF

## Slide 19: Link Layer Building Blocks
LLR, CBFC, and LLDP Format Definitions

## Slide 20: LLR Wire Formats (6 files)
Type | Format | KSY File | Size | Description
0x01 | LLR_ACK | llr_ack_ctlos.ksy | 8B | Frame acknowledgment
0x02 | LLR_NACK | llr_nack_ctlos.ksy | 8B | Negative acknowledgment
0x03 | LLR_INIT | llr_init_ctlos.ksy | 8B | Initialize sequence state
0x04 | LLR_INIT_ECHO | llr_init_echo_ctlos.ksy | 8B | Confirm initialization
- | Preamble MII | llr_preamble_mii.ksy | 8B | MII preamble format
- | Preamble 64B/66B | llr_preamble_64b66b.ksy | 8B | 64B/66B preamble format

## Slide 21: LLR Protocol State Machines (3 files)
Protocol | KSY File | UE Spec Section | Description
LLR Transmit | llr_transmit_sm.ksy | 5.1 | Transmit state machine
LLR Receive | llr_receive.ksy | 5.1 | Receive state machine
ACK/NACK Transmit | ack_nack_transmit_sm.ksy | 5.1 | ACK/NACK generation

## Slide 22: CBFC Wire Formats (2 files)
Format | KSY File | Size | Description
CF_Update | cf_update.ksy | 8B | Credit freed (CtlOS)
CC_Update | cc_update.ksy | 8B | Credit consumed (Ethernet)

## Slide 23: CBFC Protocol State Machines (3 files)
Protocol | KSY File | UE Spec Section | Description
VC State Machine | vc_state_machine.ksy | 5.2 | Virtual channel state
Lossless VC Init | lossless_vc_init.ksy | 5.2 | Lossless VC initialization
Lossless VC Removal | lossless_vc_removal.ksy | 5.2 | Lossless VC removal

## Slide 24: LLDP TLV Formats (3 files)
Format | KSY File | Description
Link Negotiation TLV | ue_link_negotiation_tlv.ksy | LLR/CBFC enable flags
CBFC TLV | ue_cbfc_tlv.ksy | VC configuration
Link Negotiation SM | link_negotiation_sm.ksy | Negotiation state machine

## Slide 25: Network and Physical Layer
Network Formats and Physical Layer Definitions

## Slide 26: Network Layer Formats (4 files)
Format | KSY File | Description
DSCP Categories | dscp_categories.ksy | DSCP category mappings
Packet Trimming | packet_trimming.ksy | Trimming mechanism
UFH 16-bit | ufh_16.ksy | 16-bit UE Fabric Header
UFH 32-bit | ufh_32.ksy | 32-bit UE Fabric Header

## Slide 27: Physical Layer Formats (1 file)
Format | KSY File | Description
Control Ordered Sets | control_ordered_sets.ksy | 64B/66B CtlOS encoding

## Slide 28: PDS Packet Variant Matrix
Delivery Modes and Response Types

## Slide 29: PDS Delivery Modes
Mode | Type | Reliability | Ordering | Use Case
RUD | 0x01 | Reliable | Unordered | General RDMA
ROD | 0x02 | Reliable | Ordered | Streaming, multi-packet
RUDI | 0x04/0x05 | Reliable | Unordered | Idempotent operations
UUD | 0x06 | Unreliable | Unordered | Best-effort traffic

## Slide 30: PDS Request/Response Mapping
Request Type | Possible Responses | KSY Files
RUD Request (0x01) | ACK, ACK_CC, ACK_CCX, NACK, NACK_CCX | rud_rod_request.ksy, rud_rod_ack.ksy, ack_cc.ksy, ack_ccx.ksy, nack.ksy, nack_ccx.ksy
ROD Request (0x02) | ACK, ACK_CC, ACK_CCX, NACK, NACK_CCX | rud_rod_request.ksy, rud_rod_ack.ksy, ack_cc.ksy, ack_ccx.ksy, nack.ksy, nack_ccx.ksy
RUDI Request (0x04) | RUDI Response, NACK | rudi_request_response.ksy, nack.ksy
UUD Request (0x06) | (no response) | uud_request.ksy
Control Packet (0x0B) | (varies by subtype) | rud_rod_cp.ksy

## Slide 31: Control Packet Subtypes
ctl_type | Name | Direction | Description
0 | NOOP | Either | No operation
1 | ACK_REQUEST | Src->Dst | Request ACK for specific PSN
2 | CLEAR_COMMAND | Init->Tgt | Clear guaranteed delivery state
3 | CLEAR_REQUEST | Tgt->Init | Request initiator to send clear
4 | CLOSE_COMMAND | Init->Tgt | PDC is being closed
5 | CLOSE_REQUEST | Tgt->Init | Request initiator to close PDC
6 | PROBE | Src->Dst | Request PDS ACK
7 | CREDIT | Dst->Src | Carry CC credit
8 | CREDIT_REQUEST | Src->Dst | Request credit
9 | NEGOTIATION | Either | PDC negotiation

## Slide 32: SES Packet Variant Matrix
Operation Types and Header Formats

## Slide 33: SES Request Opcodes
Opcode | Value | KSY File | Description
Tagged Send | 0x00 | standard_request_som1.ksy | Send with tag matching
RMA Write | 0x01 | standard_request_som1.ksy | Remote memory write
RMA Read | 0x02 | standard_request_som1.ksy | Remote memory read
Atomic Write | 0x03 | atomic_extension.ksy | Atomic memory write
Atomic Read | 0x04 | atomic_extension.ksy | Atomic memory read
Atomic CAS | 0x05 | cas_extension.ksy | Compare-and-swap
Deferrable Send | 0x06 | deferrable_send_request.ksy | Deferrable send
Ready to Restart | 0x07 | ready_to_restart.ksy | Restart notification
Small Message | 0x08 | small_message.ksy | Small message (32B header)
Small RMA Write | 0x09 | small_rma.ksy | Small RMA write
Small RMA Read | 0x0A | small_rma.ksy | Small RMA read
Small Atomic Write | 0x0B | atomic_extension.ksy | Small atomic write
Small Atomic Read | 0x0C | atomic_extension.ksy | Small atomic read
Small Atomic CAS | 0x0D | cas_extension.ksy | Small atomic CAS

## Slide 34: SES Response Opcodes
Opcode | Value | KSY File | Description
Response | 0x00 | response.ksy | Standard response
Response with Data | 0x01 | response_with_data.ksy | Response carrying data
Optimized Response | 0x02 | optimized_response_with_data.ksy | Optimized format
NACK | 0x03 | response.ksy | Negative acknowledgment

## Slide 35: Detailed Packet Structures
Wire Format Diagrams

## Slide 36: PDS Prologue (2 bytes) - prologue.ksy (text)
+-------+-------+-------+-------+-------+-------+-------+-------+
| Byte 0 | Byte 1 |
+-------+-------+-------+-------+-------+-------+-------+-------+
| type[4:0] | next_hdr/ctl[3:0] | flags[6:0] |
+-------+-------+-------+-------+-------+-------+-------+-------+

## Slide 37: RUD/ROD Request (12 bytes) - rud_rod_request.ksy (text)
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
|type |nxt|flg| clear_psn_offset | PSN [31:0] ->
+-------+-------+-------+-------+-------+-------+-------+-------+
8 9 10 11
+-------+-------+-------+-------+
-> | spdcid | dpdcid |
+-------+-------+-------+-------+

## Slide 38: ACK_CC (28 bytes) - ack_cc.ksy (text)
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
| ACK Header (12 bytes) |
+-------+-------+-------+-------+-------+-------+-------+-------+
8 9 10 11 12 13 14 15
+-------+-------+-------+-------+-------+-------+-------+-------+
| (ACK cont'd) |cc_typ|cc_flg| mpr | sack_psn_offset ->
+-------+-------+-------+-------+-------+-------+-------+-------+
16 17 18 19 20 21 22 23
+-------+-------+-------+-------+-------+-------+-------+-------+
-> | sack_bitmap [63:0] |
+-------+-------+-------+-------+-------+-------+-------+-------+
24 25 26 27
+-------+-------+-------+-------+
| ack_cc_state [63:0] |
+-------+-------+-------+-------+

## Slide 39: SES Standard Request SOM=1 (44 bytes) - standard_request_som1.ksy (text)
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
|rs|opcode |v|dc|ie|rl|hd|eo|so| message_id | ri_gen ->
+-------+-------+-------+-------+-------+-------+-------+-------+
8 9 10 11 12 13 14 15
+-------+-------+-------+-------+-------+-------+-------+-------+
-> | job_id [23:0] |rsvd|pid_on_fep |rsvd| resource_idx ->
+-------+-------+-------+-------+-------+-------+-------+-------+
16 17 18 19 20 21 22 23
+-------+-------+-------+-------+-------+-------+-------+-------+
-> | buffer_offset [63:0] |
+-------+-------+-------+-------+-------+-------+-------+-------+
24 25 26 27 28 29 30 31
+-------+-------+-------+-------+-------+-------+-------+-------+
| initiator [31:0] | match_bits / memory_key ->
+-------+-------+-------+-------+-------+-------+-------+-------+
32 33 34 35 36 37 38 39
+-------+-------+-------+-------+-------+-------+-------+-------+
-> | (match_bits cont'd) [63:0] | header_data [63:0] ->
+-------+-------+-------+-------+-------+-------+-------+-------+
40 41 42 43
+-------+-------+-------+-------+
-> | (hdr_data) | request_length|
+-------+-------+-------+-------+

## Slide 40: TSS Security Header (16 bytes, sp=1) - security_header.ksy (text)
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
|type|sp|r|an| sdi [23:0] | ssi [31:0] |
+-------+-------+-------+-------+-------+-------+-------+-------+
8 9 10 11 12 13 14 15
+-------+-------+-------+-------+-------+-------+-------+-------+
| tsc [63:0] |
| epoch [15:0] | counter [47:0] |
+-------+-------+-------+-------+-------+-------+-------+-------+

## Slide 41: LLR_ACK CtlOS (8 bytes) - llr_ack_ctlos.ksy (text)
64B/66B Block (Sync Header = 2'b10):
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
| 0x4B | 0x01 |ack_nack_seq |seq_lo | Rsvd | Rsvd | Rsvd |
| (BTF) | (ACK) | [19:12]|[11:4]|+O-code| | | |
+-------+-------+-------+-------+-------+-------+-------+-------+
D0 D1 D2 D3 D4 D5 D6 D7

## Slide 42: CF_Update CtlOS (8 bytes) - cf_update.ksy (text)
64B/66B Block (Sync Header = 2'b10):
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
| 0x5C | 0x10 |CF1_VC |CF1_cnt|CF1_cnt|CF2_VC |CF2_cnt|CF2_cnt|
| (Ctrl)| (Type)|+cnt_hi| [10:3]|lo+Ocd |+cnt_hi| [10:3]|lo+Rsvd|
+-------+-------+-------+-------+-------+-------+-------+-------+
D0 D1 D2 D3 D4 D5 D6 D7

## Slide 43: State Machines Summary
38 Protocol State Machines Across All Sublayers

## Slide 44: Transport Layer State Machines (31 files) (1/2)
Sublayer | State Machine | KSY File | States
PDS | PDC Establishment | pdc_establishment.ksy | IDLE, SYN_SENT, SYN_RCVD, ESTABLISHED
PDS | PDC Close | pdc_close.ksy | ESTABLISHED, CLOSE_WAIT, LAST_ACK, CLOSED
PDS | PDC Initiator | pdc_initiator.ksy | IDLE, CONNECTING, CONNECTED, CLOSING
PDS | PDC Target | pdc_target.ksy | IDLE, LISTENING, CONNECTED, CLOSING
PDS | PDS Manager | pds_manager.ksy | INIT, ACTIVE, SHUTDOWN
PDS | RUD Delivery | rud_delivery.ksy | IDLE, SENDING, WAITING_ACK, COMPLETE
PDS | ROD Delivery | rod_delivery.ksy | IDLE, SENDING, WAITING_ACK, COMPLETE
PDS | RUDI Delivery | rudi_delivery.ksy | IDLE, SENDING, WAITING_RESPONSE
PDS | Loss Detection CACK/SACK | loss_detection_cack_sack.ksy | MONITOR, DETECT, RETRANSMIT
PDS | Loss Detection EV | loss_detection_ev.ksy | MONITOR, VALIDATE, SIGNAL
PDS | Loss Detection NACK | loss_detection_nack.ksy | MONITOR, NACK_RCVD, RETRANSMIT
PDS | Loss Detection OOO | loss_detection_ooo.ksy | MONITOR, OOO_DETECT, SIGNAL
PDS | Loss Detection Receiver | loss_detection_receiver.ksy | MONITOR, GAP_DETECT, NACK_SEND
PDS | Loss Detection RTO | loss_detection_rto.ksy | IDLE, TIMER_RUNNING, TIMEOUT
PDS | Loss Detection Tail | loss_detection_tail.ksy | MONITOR, TAIL_DETECT, PROBE
PDS | Loss Detection Trimming | loss_detection_trimming.ksy | MONITOR, TRIM_DETECT, RETRANSMIT
CMS | CCC State Machine | ccc_state_machine.ksy | IDLE, ACTIVE, READY, PENDING
CMS | NSCC Source | nscc_source.ksy | IDLE, SLOW_START, CONG_AVOID, FAST_RECOVERY

## Slide 45: Transport Layer State Machines (31 files) (2/2)
Sublayer | State Machine | KSY File | States
CMS | NSCC Destination | nscc_destination.ksy | IDLE, MONITOR, SIGNAL_CONGESTION
CMS | RCCC Source | rccc_source.ksy | IDLE, RATE_CONTROL, BACKOFF
CMS | RCCC Destination | rccc_destination.ksy | IDLE, MONITOR_BUFFER, REQUEST_REDUCTION
CMS | TFC Source | tfc_source.ksy | IDLE, FLOW_CONTROL, THROTTLE
CMS | TFC Destination | tfc_destination.ksy | IDLE, MONITOR, SIGNAL_THROTTLE
CMS | Multipath Selection | multipath_selection.ksy | IDLE, SELECT_PATH, MONITOR_PATHS
TSS | TSS TX Processing | tss_tx_processing.ksy | IDLE, ENCRYPT, SEND
TSS | TSS RX Processing | tss_rx_processing.ksy | IDLE, DECRYPT, VALIDATE
TSS | Key Rotation | key_rotation.ksy | ACTIVE, ROTATING, COMPLETE
TSS | Join Secure Domain | join_secure_domain.ksy | INIT, JOINING, JOINED
TSS | KDF Direct | kdf_direct.ksy | INIT, DERIVE, COMPLETE
TSS | KDF Client Server | kdf_client_server.ksy | INIT, REQUEST, RECEIVE, COMPLETE
TSS | KDF Cluster | kdf_cluster.ksy | INIT, DISTRIBUTE, COMPLETE

## Slide 46: Link Layer State Machines (7 files)
Sublayer | State Machine | KSY File | States
LLR | LLR Transmit | llr_transmit_sm.ksy | IDLE, TRANSMIT, WAIT_ACK, RETRANSMIT
LLR | LLR Receive | llr_receive.ksy | IDLE, RECEIVE, VALIDATE, DELIVER
LLR | ACK/NACK Transmit | ack_nack_transmit_sm.ksy | IDLE, GENERATE, SEND
CBFC | VC State Machine | vc_state_machine.ksy | INIT, ACTIVE, PAUSED, SHUTDOWN
CBFC | Lossless VC Init | lossless_vc_init.ksy | INIT, NEGOTIATE, ACTIVE
CBFC | Lossless VC Removal | lossless_vc_removal.ksy | ACTIVE, DRAINING, REMOVED
LLDP | Link Negotiation | link_negotiation_sm.ksy | INIT, NEGOTIATE, COMPLETE

## Slide 47: Header Overhead Summary
Packet Size Analysis

## Slide 48: Minimum Header Sizes by Delivery Mode
Delivery Mode | PDS Header | SES Header | Total Overhead | KSY Files
RUD (standard) | 12B | 44B (SOM=1) | 56B | rud_rod_request.ksy, standard_request_som1.ksy
RUD (continuation) | 12B | 16B (SOM=0) | 28B | rud_rod_request.ksy, standard_request_som0.ksy
RUD (small msg) | 12B | 32B | 44B | rud_rod_request.ksy, small_message.ksy
RUD with CC | 28B | 44B (SOM=1) | 72B | rud_rod_request_cc.ksy, standard_request_som1.ksy
RUDI | 6B | 44B (SOM=1) | 50B | rudi_request_response.ksy, standard_request_som1.ksy
UUD | 6B | 44B (SOM=1) | 50B | uud_request.ksy, standard_request_som1.ksy

## Slide 49: Response Header Sizes
Response Type | PDS Header | SES Header | Total | KSY Files
ACK | 12B | - | 12B | rud_rod_ack.ksy
ACK_CC | 28B | - | 28B | ack_cc.ksy
ACK_CCX | 44B | - | 44B | ack_ccx.ksy
NACK | 12B | - | 12B | nack.ksy
NACK_CCX | 28B | - | 28B | nack_ccx.ksy
SES Response | 12B | 16B | 28B | rud_rod_ack.ksy, response.ksy
SES Response w/Data | 12B | 24B | 36B | rud_rod_ack.ksy, response_with_data.ksy
RUDI Response | 6B | 16B | 22B | rudi_request_response.ksy, response.ksy

## Slide 50: Complete Datamodel Coverage
All 103 UE KSY Files

## Slide 51: transport/pds/ (30 files) (1/2)
Category | File | Description
Format | prologue.ksy | PDS header prologue (2B)
Format | rud_rod_request.ksy | RUD/ROD request (12B)
Format | rud_rod_request_cc.ksy | RUD/ROD request with CC (28B)
Format | rudi_request_response.ksy | RUDI request/response (6B)
Format | uud_request.ksy | UUD request (6B)
Format | rud_rod_ack.ksy | ACK (12B)
Format | ack_cc.ksy | ACK_CC (28B)
Format | ack_ccx.ksy | ACK_CCX (44B)
Format | nack.ksy | NACK (12B)
Format | nack_ccx.ksy | NACK_CCX (28B)
Format | nack_codes.ksy | NACK reason codes
Format | rud_rod_cp.ksy | Control packet (12B)
Format | entropy_header.ksy | Entropy header (4B)
Format | rud_rod_default_ses.ksy | Default SES response (8B)
Protocol | pdc_establishment.ksy | PDC establishment SM
Protocol | pdc_close.ksy | PDC close SM
Protocol | pdc_initiator.ksy | PDC initiator SM
Protocol | pdc_target.ksy | PDC target SM

## Slide 52: transport/pds/ (30 files) (2/2)
Category | File | Description
Protocol | pds_manager.ksy | PDS manager SM
Protocol | rud_delivery.ksy | RUD delivery SM
Protocol | rod_delivery.ksy | ROD delivery SM
Protocol | rudi_delivery.ksy | RUDI delivery SM
Protocol | loss_detection_cack_sack.ksy | CACK/SACK loss detection
Protocol | loss_detection_ev.ksy | Early validation loss detection
Protocol | loss_detection_nack.ksy | NACK loss detection
Protocol | loss_detection_ooo.ksy | OOO loss detection
Protocol | loss_detection_receiver.ksy | Receiver loss detection
Protocol | loss_detection_rto.ksy | RTO loss detection
Protocol | loss_detection_tail.ksy | Tail loss detection
Protocol | loss_detection_trimming.ksy | Trimming loss detection

## Slide 53: transport/ses/ (27 files) (1/2)
Category | File | Description
Format | standard_request_som1.ksy | Standard request SOM=1 (44B)
Format | standard_request_som0.ksy | Standard request SOM=0 (16B)
Format | optimized_non_matching.ksy | Optimized non-matching (32B)
Format | small_message.ksy | Small message (32B)
Format | small_rma.ksy | Small RMA (32B)
Format | response.ksy | Response (16B)
Format | response_with_data.ksy | Response with data (24B)
Format | optimized_response_with_data.ksy | Optimized response (16B)
Format | rendezvous_extension.ksy | Rendezvous extension (32B)
Format | atomic_extension.ksy | Atomic extension (8B)
Format | cas_extension.ksy | CAS extension (40B)
Format | deferrable_send_request.ksy | Deferrable send (44B)
Format | ready_to_restart.ksy | Ready to restart (44B)
Format | opcodes.ksy | SES opcodes
Format | next_header_types.ksy | Next header types
Sequence | single_packet_request.ksy | Single packet request
Sequence | multi_packet_request.ksy | Multi packet request
Sequence | read_standard.ksy | Standard read

## Slide 54: transport/ses/ (27 files) (2/2)
Category | File | Description
Sequence | read_large_ack.ksy | Large read with ACK
Sequence | rendezvous_expected.ksy | Rendezvous expected
Sequence | rendezvous_unexpected.ksy | Rendezvous unexpected
Sequence | deferrable_expected.ksy | Deferrable expected
Sequence | deferrable_unexpected.ksy | Deferrable unexpected
Sequence | deferrable_no_buffer.ksy | Deferrable no buffer
Sequence | buffered_messages.ksy | Buffered messages
Sequence | buffered_headers.ksy | Buffered headers
Sequence | backoff_retry.ksy | Backoff retry

## Slide 55: transport/cms/ (15 files)
Category | File | Description
Format | ack_cc_state_nscc.ksy | NSCC CC state (8B)
Format | ack_cc_state_rccc_tfc.ksy | RCCC/TFC CC state (8B)
Format | req_cc_state.ksy | Request CC state (8B)
Format | credit_cp_payload.ksy | Credit CP payload
Format | credit_request_cp_payload.ksy | Credit request payload
Format | cc_type.ksy | CC type enum
Format | ccx_type.ksy | CCX type enum
Protocol | ccc_state_machine.ksy | CCC state machine
Protocol | nscc_source.ksy | NSCC source
Protocol | nscc_destination.ksy | NSCC destination
Protocol | rccc_source.ksy | RCCC source
Protocol | rccc_destination.ksy | RCCC destination
Protocol | tfc_source.ksy | TFC source
Protocol | tfc_destination.ksy | TFC destination
Protocol | multipath_selection.ksy | Multipath selection

## Slide 56: transport/tss/ (9 files)
Category | File | Description
Format | security_header.ksy | Security header (12-16B)
Format | iv_construction.ksy | IV construction (12B)
Protocol | tss_tx_processing.ksy | TX processing
Protocol | tss_rx_processing.ksy | RX processing
Protocol | key_rotation.ksy | Key rotation
Protocol | join_secure_domain.ksy | Join secure domain
Protocol | kdf_direct.ksy | KDF direct
Protocol | kdf_client_server.ksy | KDF client-server
Protocol | kdf_cluster.ksy | KDF cluster

## Slide 57: link/llr/ (9 files)
Category | File | Description
Format | llr_ack_ctlos.ksy | LLR_ACK CtlOS (8B)
Format | llr_nack_ctlos.ksy | LLR_NACK CtlOS (8B)
Format | llr_init_ctlos.ksy | LLR_INIT CtlOS (8B)
Format | llr_init_echo_ctlos.ksy | LLR_INIT_ECHO CtlOS (8B)
Format | llr_preamble_mii.ksy | LLR preamble MII (8B)
Format | llr_preamble_64b66b.ksy | LLR preamble 64B/66B (8B)
Protocol | llr_transmit_sm.ksy | LLR transmit SM
Protocol | llr_receive.ksy | LLR receive SM
Protocol | ack_nack_transmit_sm.ksy | ACK/NACK transmit SM

## Slide 58: link/cbfc/ (5 files)
Category | File | Description
Format | cf_update.ksy | CF_Update CtlOS (8B)
Format | cc_update.ksy | CC_Update message (8B)
Protocol | vc_state_machine.ksy | VC state machine
Protocol | lossless_vc_init.ksy | Lossless VC init
Protocol | lossless_vc_removal.ksy | Lossless VC removal

## Slide 59: link/lldp/ (3 files)
Category | File | Description
Format | ue_link_negotiation_tlv.ksy | Link negotiation TLV
Format | ue_cbfc_tlv.ksy | CBFC TLV
Protocol | link_negotiation_sm.ksy | Link negotiation SM

## Slide 60: network/ (4 files)
Category | File | Description
Format | dscp_categories.ksy | DSCP categories
Format | packet_trimming.ksy | Packet trimming
Format | ufh_16.ksy | UFH 16-bit
Format | ufh_32.ksy | UFH 32-bit

## Slide 61: physical/ (1 file)
Category | File | Description
Format | control_ordered_sets.ksy | Control Ordered Sets

## Slide 62: Detailed Header Formats
Field-level documentation with packet diagrams

## Slide 63: LLR Preamble 64B/66B Block Format
8 bytes (64 bits)

## Slide 64: llr_preamble_64b66b Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| sequence_number | control_flags|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| reserved |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 65: llr_preamble_64b66b Field Definitions
Field | Bits | Offset | Type | Description
sequence_number | 24 | 0 | b24 | Sequence number (24 bits). LLR frame sequence number.
control_flags | 8 | 24 | u1 | Control flags (8 bits). LLR-specific control.
reserved | 32 | 32 |  | Reserved (32 bits). MUST be 0.

## Slide 66: LLR_ACK Control Ordered Set (CtlOS)
8 bytes (64 bits)

## Slide 67: llr_ack_ctlos Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| block_type | ctlos_type |ack_nack_seq_hi|ack_nack_seq_m|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|ack_nack_seq_lo| reserved_d5 | reserved_d6 | reserved_d7 |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 68: llr_ack_ctlos Field Definitions
Field | Bits | Offset | Type | Description
block_type | 8 | 0 | u1 | Block Type Field for 64B/66B control block.
ctlos_type | 8 | 8 | u1 | CtlOS Message Type identifier.
ack_nack_seq_high | 8 | 16 | u1 | ACK/NACK sequence number bits [19:12] (upper 8 bits).
ack_nack_seq_mid | 8 | 24 | u1 | ACK/NACK sequence number bits [11:4] (middle 8 bits).
ack_nack_seq_low_and_ocode | 8 | 32 | u1 | Combined field containing:
reserved_d5 | 8 | 40 | u1 | Reserved field. MUST be 0x00.
reserved_d6 | 8 | 48 | u1 | Reserved field. MUST be 0x00.
reserved_d7 | 8 | 56 | u1 | Reserved field. MUST be 0x00.

## Slide 69: LLR_NACK Control Ordered Set (CtlOS)
8 bytes (64 bits)

## Slide 70: llr_nack_ctlos Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| block_type | ctlos_type |ack_nack_seq_hi|ack_nack_seq_m|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|ack_nack_seq_lo| reserved_d5 | reserved_d6 | reserved_d7 |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 71: llr_nack_ctlos Field Definitions
Field | Bits | Offset | Type | Description
block_type | 8 | 0 | u1 | Block Type Field for 64B/66B control block. MUST be 0x4B.
ctlos_type | 8 | 8 | u1 | CtlOS Message Type identifier. MUST be 0x02 for LLR_NACK.
ack_nack_seq_high | 8 | 16 | u1 | ACK/NACK sequence number bits [19:12] (upper 8 bits).
ack_nack_seq_mid | 8 | 24 | u1 | ACK/NACK sequence number bits [11:4] (middle 8 bits).
ack_nack_seq_low_and_ocode | 8 | 32 | u1 | Combined field: ack_nack_seq[3:0] (upper nibble) + O-code (l
reserved_d5 | 8 | 40 | u1 | Reserved field. MUST be 0x00.
reserved_d6 | 8 | 48 | u1 | Reserved field. MUST be 0x00.
reserved_d7 | 8 | 56 | u1 | Reserved field. MUST be 0x00.

## Slide 72: CBFC CF_Update Control Ordered Set (CtlOS)
8 bytes (64 bits)

## Slide 73: cbfc_cf_update Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| control_char | message_type |cf1_vc_and_coun| cf1_count_mid|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|cf1_count_low_a|cf2_vc_and_coun| cf2_count_mid |cf2_count_low_|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 74: cbfc_cf_update Field Definitions
Field | Bits | Offset | Type | Description
control_char | 8 | 0 | u1 | Control character value for UE control ordered set.
message_type | 8 | 8 | u1 | CtlOS Message Type identifier.
cf1_vc_and_count_high | 8 | 16 | u1 | Combined field containing:
cf1_count_mid | 8 | 24 | u1 | CF1 credit count bits [10:3] (middle 8 bits of 15-bit count)
cf1_count_low_and_ocode | 8 | 32 | u1 | Combined field containing:
cf2_vc_and_count_high | 8 | 40 | u1 | Combined field containing:
cf2_count_mid | 8 | 48 | u1 | CF2 credit count bits [10:3] (middle 8 bits of 15-bit count)
cf2_count_low_and_reserved | 8 | 56 | u1 | Combined field containing:

## Slide 75: CBFC CC_Update Message
8 bytes (64 bits)

## Slide 76: cbfc_cc_update Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| message_type |vc_index_and_cc|cc_counter_mid |cc_counter_low|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| reserved |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 77: cbfc_cc_update Field Definitions
Field | Bits | Offset | Type | Description
message_type | 8 | 0 | u1 | Message type identifier for CC_Update.
vc_index_and_cc_high | 8 | 8 | u1 | Combined field:
cc_counter_mid | 8 | 16 | u1 | CC counter middle 8 bits.
cc_counter_low | 8 | 24 | u1 | CC counter lower 4 bits (upper nibble).
reserved | 32 | 32 |  | Reserved (32 bits). MUST be 0.

## Slide 78: UE Link Negotiation Options TLV
5 bytes (40 bits)

## Slide 79: ue_link_negotiation_tlv Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| tlv_type | tlv_length | subtype |l|c| reserved |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| ue_version |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 80: ue_link_negotiation_tlv Field Definitions
Field | Bits | Offset | Type | Description
tlv_type | 7 | 0 | b7 | TLV Type = 127 (Organizationally Specific TLV).
tlv_length | 9 | 7 | b9 | TLV Length in octets (variable, includes OUI + Subtype + Val
oui | 0 | 16 | u3 | Organizationally Unique Identifier (OUI) for Ultra Ethernet
subtype | 8 | 16 | u1 | UE-specific subtype = 1 (Link Negotiation Options).
llr_enabled | 1 | 24 | b1 | Link Layer Retry (LLR) enabled flag.
cbfc_enabled | 1 | 25 | b1 | Credit-Based Flow Control (CBFC) enabled flag.
reserved | 6 | 26 | b6 | Reserved bits, must be 0.
ue_version | 8 | 32 | u1 | UE Specification version supported.

## Slide 81: UE CBFC TLV
12 bytes (96 bits)

## Slide 82: ue_cbfc_tlv Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| tlv_type | tlv_length | subtype | num_vcs |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| credit_pool_size | lossless_vcs |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| lossless_vcs | reserved |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 83: ue_cbfc_tlv Field Definitions
Field | Bits | Offset | Type | Description
tlv_type | 7 | 0 | b7 | TLV Type = 127 (Organizationally Specific TLV).
tlv_length | 9 | 7 | b9 | TLV Length in octets (variable, includes OUI + Subtype + Val
oui | 0 | 16 | u3 | Organizationally Unique Identifier (OUI) for Ultra Ethernet
subtype | 8 | 16 | u1 | UE-specific subtype = 2 (CBFC Configuration).
num_vcs | 8 | 24 | u1 | Number of virtual channels (VCs) supported.
credit_pool_size | 16 | 32 | u2 | Total credit pool size (in credits).
lossless_vcs | 32 | 48 | u4 | Bitmap of lossless VCs (bit N = 1 if VC N is lossless).
reserved | 16 | 80 | u2 | Reserved bytes, must be 0.

## Slide 84: References
Specification and Documentation Sources

## Slide 85: Primary References
• UE Specification v1.0.1, Chapter 3 (Transport Layer)
• UE Specification v1.0.1, Chapter 4 (Network Layer)
• UE Specification v1.0.1, Chapter 5 (Link Layer)
• UE Specification v1.0.1, Section 3.4 (SES)
• UE Specification v1.0.1, Section 3.5 (PDS)
• UE Specification v1.0.1, Section 3.6 (CMS)
• UE Specification v1.0.1, Section 3.7 (TSS)
• UE Specification v1.0.1, Section 5.1 (LLR)
• UE Specification v1.0.1, Section 5.2 (CBFC)
• IEEE 802.3-2022, Clause 82.2.3 (64B/66B Block Format)

## Slide 86: Analysis Documents
• analysis/packet_taxonomy/packet_taxonomy_ue_pds.md - PDS format details
• analysis/packet_taxonomy/packet_taxonomy_ue_ses.md - SES format details
• analysis/packet_taxonomy/packet_taxonomy_ue_cms_tss.md - CMS/TSS format details
• analysis/packet_taxonomy/packet_taxonomy_ue_link.md - Link layer format details

## Slide 87: Datamodel Location
• earlysim/datamodel/protocols/ue/transport/pds/ - 30 PDS files
• earlysim/datamodel/protocols/ue/transport/ses/ - 27 SES files
• earlysim/datamodel/protocols/ue/transport/cms/ - 15 CMS files
• earlysim/datamodel/protocols/ue/transport/tss/ - 9 TSS files
• earlysim/datamodel/protocols/ue/link/llr/ - 9 LLR files
• earlysim/datamodel/protocols/ue/link/cbfc/ - 5 CBFC files
• earlysim/datamodel/protocols/ue/link/lldp/ - 3 LLDP files
• earlysim/datamodel/protocols/ue/network/ - 4 network files
• earlysim/datamodel/protocols/ue/physical/ - 1 physical file