## Slide 1: PMR Packet Taxonomy: Cornelis Proprietary Technical Report
Cornelis Networks UE+ Extensions and HMAC Addressing
Packet Taxonomy Team
Cornelis Networks Engineering

## Slide 2: Table of Contents
Overview
Protocol Architecture
Header Building Blocks
UE+ Header Structure
UFH-16+ and UFH-32+ Headers
CSIG+ Telemetry
L2 Header Selection State Machine
HMAC Addressing Formats
Header Overhead Summary
Datamodel Coverage
Detailed Header Formats
UFH-16+ Unified Forwarding Header (16-bit Add...
UFH-32+ Unified Forwarding Header (32-bit Add...
Cornelis Ethernet L2 Prefix
UE+ Optimized Ultra Ethernet L2 Header
CSIG+ Telemetry Header
PKEY Partition Key Stacked Header
References

## Slide 3: Overview
Cornelis UE+ Extensions for High-Performance Fabric

## Slide 4: Cornelis Proprietary Formats

## Slide 5: Cornelis Format Summary
Layer | Format | Size | Status | KSY File
Link | UE+ Header | 12 bytes | Complete | ue_plus.ksy
Link | Cornelis L2 Prefix | 1 byte | Complete | cornelis_l2_prefix.ksy
Network | UFH-16+ | 12 bytes | Complete | ufh_16_plus.ksy
Network | UFH-32+ | 12 bytes | Complete | ufh_32_plus.ksy
Network | Collective L2 | 4 bytes | WIP | collective_l2.ksy
Network | Scale-Up L2 | 4 bytes | WIP | scaleup_l2.ksy
Transport | CSIG+ | 4 bytes | Complete | csig_plus.ksy
Transport | PKEY | 2 bytes | Complete | pkey.ksy
Config | Address Vector | 32 bytes | Complete | address_vector.ksy
Config | Peer Capability | 32 bytes | Complete | peer_capability.ksy
Protocol | L2 Header Selection SM | N/A | Complete | l2_header_selection_sm.ksy
Encapsulation | VxLAN+ | 4 bytes | Complete | vxlan_plus.ksy

## Slide 6: Protocol Architecture
UE+ vs Standard UE Comparison

## Slide 7: UE+ vs Standard UE
Aspect | UE+ (Cornelis) | Standard UE
L2 Header | 12-byte UE+ with HMAC | 14-byte Ethernet II
Addressing | 24-bit Hierarchical MAC | 48-bit MAC + IPv4/IPv6
Telemetry | CSIG+ in-band (optional) | None
Transport | Standard UE PDS/SES/CMS/TSS | Standard UE PDS/SES/CMS/TSS
Security | TSS encryption (UE standard) | TSS encryption (UE standard)
FEP Mode | IPv4/UDP encapsulation | IPv4/UDP encapsulation

## Slide 8: Key Architecture Principle (HFI_ARCH_003)

## Slide 9: Header Building Blocks
All 12 Cornelis KSY Files with Sizes

## Slide 10: Link Layer Headers
Header | Size | KSY File | Description
UE+ L2 | 12 bytes | cornelis/link/ue_plus.ksy | Optimized L2 header with 24-bit HMAC
Cornelis L2 Prefix | 1 byte | cornelis/link/cornelis_l2_prefix.ksy | Prefix for encapsulated Ethernet frames

## Slide 11: Network Layer Headers
Header | Size | KSY File | Description
UFH-16+ | 12 bytes | cornelis/network/ufh_16_plus.ksy | 16-bit forwarding (65K endpoints)
UFH-32+ | 12 bytes | cornelis/network/ufh_32_plus.ksy | 32-bit forwarding (4B+ endpoints)
Collective L2 | 4 bytes | cornelis/network/collective_l2.ksy | HW-accelerated collectives (WIP)
Scale-Up L2 | 4 bytes | cornelis/network/scaleup_l2.ksy | GPU cluster interconnect (WIP)

## Slide 12: Transport and Config Headers
Header | Size | KSY File | Description
CSIG+ | 4 bytes | cornelis/transport/csig_plus.ksy | In-band telemetry header
PKEY | 2 bytes | cornelis/transport/pkey.ksy | Partition key isolation
Address Vector | 32 bytes | cornelis/config/address_vector.ksy | Per-destination protocol config
Peer Capability | 32 bytes | cornelis/config/peer_capability.ksy | Per-peer capability state

## Slide 13: Protocol and Encapsulation
Header | Size | KSY File | Description
L2 Header Selection SM | N/A | cornelis/protocols/l2_header_selection_sm.ksy | L2 header selection decision logic
VxLAN+ | 4 bytes | cornelis/encapsulation/vxlan_plus.ksy | Fabric-aware overlay networking

## Slide 14: UE+ Header Structure
12-Byte Optimized L2 Header (ue_plus.ksy)

## Slide 15: UE+ Header Field Layout
Field | Bits | Byte.Bit | Description
L2 | 2 | 0[7:6] | L2 type identifier (CSR-configurable)
V | 2 | 0[5:4] | Version field
zyxm | 4 | 0[3:0] | Local MAC indicator (0b0010 for UE+)
Length | 6 | 1[7:2] | Packet length (units TBD)
RC | 3 | 1[1:0], 2[7] | Routing Class (split across bytes)
SC | 4 | 2[6:3] | Service Class
Hop | 3 | 2[2:0] | Hop count (0-7)
DLID/DMAC | 24 | 3-5 | Destination Hierarchical MAC
Entropy | 16 | 6-7 | ECMP load balancing hash
Reserved | 8 | 8 | Reserved for future use
SLID/SMAC | 24 | 9-11 | Source Hierarchical MAC

## Slide 16: UE+ Terminology Mapping

## Slide 17: UFH-16+ and UFH-32+ Headers
Unified Forwarding Headers (ufh_16_plus.ksy, ufh_32_plus.ksy)

## Slide 18: UFH-16+ Field Layout (12 bytes)
Field | Byte(s) | Bits | Description
Type | 0 | [7:4] | Packet type for forwarding
SLAP (dest) | 0 | [3:0] | Z,Y,X,M bits (Z,Y,X=001)
Opaque | 1-3 | 24 | Opaque to hardware
Destination | 4-5 | 16 | Destination address (big-endian)
Opaque | 6 | [7:4] | Opaque to hardware
SLAP (src) | 6 | [3:0] | Z,Y,X,M bits (Z,Y,X=001)
Traffic Class | 7 | [7:0] | QoS/priority classification
Opaque | 8-9 | 16 | Opaque to hardware
Source | 10-11 | 16 | Source address (big-endian)

## Slide 19: UFH-32+ Field Layout (12 bytes)
Field | Byte(s) | Bits | Description
Type | 0 | [7:4] | Packet type for forwarding
SLAP (dest) | 0 | [3:0] | Z,Y,X,M bits (Z,Y,X=001)
Opaque | 1 | [7:0] | Opaque to hardware
Destination | 2-5 | 32 | Destination address (big-endian)
Hop Limit | 6 | [7:4] | TTL/hop count
SLAP (src) | 6 | [3:0] | Z,Y,X,M bits (Z,Y,X=001)
Traffic Class | 7 | [7:0] | QoS/priority classification
Source | 8-11 | 32 | Source address (big-endian)

## Slide 20: UFH Type Values
Value | Type | Description
0 | Data | Data packet
1 | Control | Control packet
2 | Collective | Collective operation packet
3 | Credit | Credit/flow control
4 | Management | Management packet
5 | Multicast | Multicast packet (UFH-32 only)
6 | Barrier | Barrier synchronization (UFH-32 only)
7 | Reduction | Reduction operation (UFH-32 only)
15 | Extended/Vendor | UFH-32 extension (UFH-16) or Vendor (UFH-32)

## Slide 21: CSIG+ Telemetry
In-Band Network Monitoring (csig_plus.ksy)

## Slide 22: CSIG+ Header Layout (4 bytes)
Field | Bits | Offset | Description
Version | 4 | 0[7:4] | CSIG+ version (must be 0)
Telemetry Type | 4 | 0[3:0] | Type of telemetry data
Flags | 8 | 1[7:0] | Control flags
Telemetry Data | 16 | 2-3 | Type-specific data

## Slide 23: CSIG+ Telemetry Types
Value | Type | Data Format | Use Case
0 | Latency | Accumulated ns (16-bit) | Per-hop latency measurement
1 | Queue Depth | Occupancy % + QID | Queue monitoring
2 | Congestion | ECN + Level | Congestion notification
3 | Path Trace | Switch ID (16-bit) | Path verification
4 | Timestamp | Truncated time (16-bit) | Timing correlation
15 | Custom | Vendor-defined | Vendor extensions

## Slide 24: CSIG+ Flags
Bit | Name | Description
7 | Accumulate | Add hop data (vs replace)
6 | Report | Generate telemetry report
5 | Sink | Final hop for telemetry
4 | Source | Originating hop
3:0 | Type-specific | Varies by telemetry type

## Slide 25: L2 Header Selection State Machine
Decision Logic (l2_header_selection_sm.ksy)

## Slide 26: L2 Header Selection Decision Tree
Order | Condition | Result | Reason
1 | packet_type == ROCEV2 | ETHERNET_II | RoCEv2 always uses Ethernet + IP + UDP
2 | packet_type == ETHERNET_SERVICE | ETHERNET_II | PTP, management, netdev use standard Ethernet
3 | link_state != UE_PLUS_ENABLED | ETHERNET_II | Link did not negotiate UE+ capability
4 | !av_entry.ue_plus_capable | ETHERNET_II | Destination does not support UE+
5 | !av_entry.hmac_valid | ETHERNET_II | No fabric-managed HMAC for destination
6 | av_entry.protocol_type == UE_STANDARD | ETHERNET_II | AV configured for standard UE over UDP
7 | default | UE_PLUS | All conditions met for UE+ header

## Slide 27: L2 Header Selection Inputs
Input | Type | Source
link_state | link_negotiation_state_enum | link_negotiation_sm.ksy
av_entry | address_vector_entry | address_vector.ksy
packet_type | packet_type_enum | Application request

## Slide 28: HMAC Addressing Formats
3 Topology Configurations

## Slide 29: HMAC Address Topologies
Topology | Group Bits | Switch Bits | Terminal Bits | Total
No subdivision | 12 (0-4095) | 6 (0-63) | 6 (0-63) | 24 bits
x2 NIC subdivision | 11 (0-2047) | 6 (0-63) | 7 (0-127) | 24 bits
x8 NIC subdivision | 9 (0-511) | 6 (0-63) | 9 (0-511) | 24 bits

## Slide 30: HMAC Address Structure

## Slide 31: Header Overhead Summary
Packet Variant Efficiency Analysis

## Slide 32: UE+ Packet Variant Overhead
Variant | L2 | Telemetry | Security | Transport | Total | 4KB Efficiency
UE+ Standard | 12 | 0 | 0 | 88 | 100 | 97.6%
UE+ Small | 12 | 0 | 0 | 56 | 68 | 98.4%
UE+ + CSIG+ | 12 | 4 | 0 | 88 | 104 | 97.5%
UE+ Encrypted | 12 | 0 | 16+16 | 88 | 132 | 96.9%
UE+ IPv4 | 42 | 0 | 0 | 88 | 130 | 96.9%
UE+ IPv4 Encrypted | 42 | 0 | 16+16 | 88 | 162 | 96.2%
UE+ Full Stack | 12 | 4 | 16+16 | 88 | 136 | 96.8%

## Slide 33: Protocol Comparison
Protocol | Min Overhead | Max Overhead | 4KB Efficiency
UE+ Standard | 100 bytes | 100 bytes | 97.6%
UE+ Small | 68 bytes | 68 bytes | 98.4%
RoCEv2 (IPv4) | 58 bytes | 78 bytes | 98.6%
RoCEv2 (IPv6) | 78 bytes | 98 bytes | 98.1%

## Slide 34: Datamodel Coverage
All 12 Cornelis KSY Files

## Slide 35: Cornelis KSY File Summary
Category | File | Lines | Status
Link | ue_plus.ksy | 394 | Complete
Link | cornelis_l2_prefix.ksy | 131 | Complete
Network | ufh_16_plus.ksy | 244 | Complete
Network | ufh_32_plus.ksy | 240 | Complete
Network | collective_l2.ksy | 277 | WIP
Network | scaleup_l2.ksy | 221 | WIP
Transport | csig_plus.ksy | 202 | Complete
Transport | pkey.ksy | 120 | Complete
Config | address_vector.ksy | 199 | Complete
Config | peer_capability.ksy | 194 | Complete
Protocol | l2_header_selection_sm.ksy | 222 | Complete
Encapsulation | vxlan_plus.ksy | 137 | Complete

## Slide 36: Datamodel Directory Structure

## Slide 37: Detailed Header Formats
Field-level documentation with packet diagrams

## Slide 38: UFH-16+ Unified Forwarding Header (16-bit Addressing) - Cornelis Extension
12 bytes (96 bits)

## Slide 39: ufh_16_plus Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|ufh_typ|slap_de| opaque_dest |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| destination |opaque_|slap_sr| traffic_class|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| opaque_src | source |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 40: ufh_16_plus Field Definitions
Field | Bits | Offset | Type | Description
ufh_type | 4 | 0 | b4 | UFH Type (4 bits).
slap_dest | 4 | 4 | b4 | SLAP field for MAC Destination (4 bits).
opaque_dest | 24 | 8 |  | Opaque field (24 bits / 3 bytes).
destination | 16 | 32 | u2 | Destination Address (16 bits, big-endian).
opaque_6_high | 4 | 48 | b4 | Opaque field (4 bits).
slap_src | 4 | 52 | b4 | SLAP field for MAC Source (4 bits).
traffic_class | 8 | 56 | u1 | Traffic Class (8 bits).
opaque_src | 16 | 64 | u2 | Opaque field (16 bits).
source | 16 | 80 | u2 | Source Address (16 bits, big-endian).

## Slide 41: UFH-32+ Unified Forwarding Header (32-bit Addressing) - Cornelis Extension
12 bytes (96 bits)

## Slide 42: ufh_32_plus Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|ufh_typ|slap_de| opaque | destination |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| destination |hop_lim|slap_sr| traffic_class|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| source |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 43: ufh_32_plus Field Definitions
Field | Bits | Offset | Type | Description
ufh_type | 4 | 0 | b4 | UFH Type (4 bits).
slap_dest | 4 | 4 | b4 | SLAP field for MAC Destination (4 bits).
opaque | 8 | 8 | u1 | Opaque field (8 bits).
destination | 32 | 16 | u4 | Destination Address (32 bits, big-endian).
hop_limit | 4 | 48 | b4 | Hop Limit (4 bits).
slap_src | 4 | 52 | b4 | SLAP field for MAC Source (4 bits).
traffic_class | 8 | 56 | u1 | Traffic Class (8 bits).
source | 32 | 64 | u4 | Source Address (32 bits, big-endian).

## Slide 44: Cornelis Ethernet L2 Prefix
1 bytes (8 bits)

## Slide 45: cornelis_l2_prefix Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|l2_|pri| flags |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 46: cornelis_l2_prefix Field Definitions
Field | Bits | Offset | Type | Description
l2_type | 2 | 0 | b2 | L2 Type (2 bits).
priority | 2 | 2 | b2 | Priority (2 bits).
flags | 4 | 4 | b4 | Flags (4 bits).

## Slide 47: UE+ Optimized Ultra Ethernet L2 Header
12 bytes (96 bits)

## Slide 48: ue_plus_header Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|l2_|ver| zyxm | length |rc_|r|service|hop_c| dest_hmac |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dest_hmac | entropy |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| reserved | source_hmac |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 49: ue_plus_header Field Definitions
Field | Bits | Offset | Type | Description
l2_type | 2 | 0 | b2 | L2 Type Identifier (2 bits).
version | 2 | 2 | b2 | Version field (2 bits).
zyxm | 4 | 4 | b4 | Local MAC indicator (4 bits).
length | 6 | 8 | b6 | Packet length (6 bits).
rc_high | 2 | 14 | b2 | Routing Class high bits (2 bits).
rc_low | 1 | 16 | b1 | Routing Class low bit (1 bit).
service_class | 4 | 17 | b4 | Service Class (4 bits).
hop_count | 3 | 21 | b3 | Hop Count (3 bits).
dest_hmac | 24 | 24 | b24 | Destination Hierarchical MAC (24 bits).
entropy | 16 | 48 | u2 | Entropy field (16 bits).
reserved | 8 | 64 | u1 | Reserved field (8 bits).
source_hmac | 24 | 72 | b24 | Source Hierarchical MAC (24 bits).

## Slide 50: CSIG+ Telemetry Header
4 bytes (32 bits)

## Slide 51: csig_plus Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|version|telemet| flags | telemetry_data |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 52: csig_plus Field Definitions
Field | Bits | Offset | Type | Description
version | 4 | 0 | b4 | Version (4 bits).
telemetry_type | 4 | 4 | b4 | Telemetry Type (4 bits).
flags | 8 | 8 | u1 | Flags (8 bits).
telemetry_data | 16 | 16 | u2 | Telemetry Data (16 bits).

## Slide 53: PKEY Partition Key Stacked Header
2 bytes (16 bits)

## Slide 54: pkey Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|m| pkey_high | pkey_low |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 55: pkey Field Definitions
Field | Bits | Offset | Type | Description
membership | 1 | 0 | b1 | Membership Type (1 bit).
pkey_high | 7 | 1 | b7 | P_Key High Bits (7 bits).
pkey_low | 8 | 8 | u1 | P_Key Low Byte (8 bits).

## Slide 56: References
Documentation and Specifications

## Slide 57: Internal Documents
Document | Description
packet_taxonomy_cornelis.md | Cornelis proprietary formats detail
packet_taxonomy_ue_plus_variants.md | UE+ packet variants analysis
CN7000 Packet Taxonomy.ppt | Original PowerPoint reference
CN7000 HFI Requirements | HFI_ARCH_003 simultaneous protocol support

## Slide 58: External Specifications
Specification | Version | Sections
UE Specification | v1.0.1 | Table 3-16 (next_hdr), Table 3-90 (TSS)
Cornelis UE+ Specification | 1.1 | UE+ L2 Header, CSIG+ Telemetry
RFC 7348 | N/A | VxLAN standard
IEEE 802.1Q | N/A | VLAN tagging

## Slide 59: KSY File References (All 12)