## Slide 1: PMR Packet Taxonomy: RoCEv2 Technical Report
RDMA over Converged Ethernet v2 Protocol Formats
Packet Taxonomy Team
Cornelis Networks Engineering

## Slide 2: Table of Contents
RoCEv2 Overview
RoCEv2 Packet Variants
Header Overhead Summary
Protocol Architecture
Header Building Blocks
Base Transport Header (BTH)
Packet Variant Matrix
RETH - RDMA Extended Transport Header
AETH - ACK Extended Transport Header
AtomicETH - Atomic Extended Transport Header
QP State Machine
Operation Validity Matrix
Header Overhead Summary
ICRC - Invariant CRC
Datamodel Coverage
Detailed Header Formats
RoCEv2 Base Transport Header
RoCEv2 RDMA Extended Transport Header
RoCEv2 ACK Extended Transport Header
RoCEv2 Datagram Extended Transport Header
RoCEv2 Atomic Extended Transport Header
RoCEv2 Immediate Data
References

## Slide 3: RoCEv2 Overview
RDMA over Converged Ethernet v2 Characteristics

## Slide 4: RoCEv2 Key Characteristics

## Slide 5: PMR Supported Transport Types
Type | Value | Description | PMR Support
RC | 0x00 | Reliable Connection | Yes
UC | 0x20 | Unreliable Connection | Yes
RD | 0x40 | Reliable Datagram | Yes
UD | 0x60 | Unreliable Datagram | Yes
CNP | 0x80 | Congestion Notification Packet (ECN) | Yes
XRC | 0xA0 | Extended Reliable Connection | No - Not Supported

## Slide 6: RoCEv2 Packet Variants
Complete packet type matrix with header stacks

## Slide 7: RC (Reliable Connection) Packet Variants
Variant | Header Stack | Total Overhead | Use Case
RC SEND_ONLY | Eth → IPv4 → UDP → BTH → ICRC | 58B | Single-packet send
RC SEND_ONLY_IMM | Eth → IPv4 → UDP → BTH → ImmDt → ICRC | 62B | Send with immediate data
RC SEND_FIRST/MIDDLE/LAST | Eth → IPv4 → UDP → BTH → ICRC | 58B | Multi-packet send
RC RDMA_WRITE_ONLY | Eth → IPv4 → UDP → BTH → RETH → ICRC | 74B | Single-packet RDMA write
RC RDMA_WRITE_ONLY_IMM | Eth → IPv4 → UDP → BTH → RETH → ImmDt → ICRC | 78B | RDMA write with immediate
RC RDMA_WRITE_FIRST | Eth → IPv4 → UDP → BTH → RETH → ICRC | 74B | First packet of multi-packet write
RC RDMA_WRITE_MIDDLE/LAST | Eth → IPv4 → UDP → BTH → ICRC | 58B | Continuation packets
RC RDMA_READ_REQUEST | Eth → IPv4 → UDP → BTH → RETH → ICRC | 74B | RDMA read request (no payload)
RC RDMA_READ_RESPONSE | Eth → IPv4 → UDP → BTH → AETH → ICRC | 62B | RDMA read response with data
RC ACK | Eth → IPv4 → UDP → BTH → AETH → ICRC | 62B | Acknowledgment (no payload)
RC CMP_SWAP | Eth → IPv4 → UDP → BTH → AtomicETH → ICRC | 86B | Compare-and-swap atomic
RC FETCH_ADD | Eth → IPv4 → UDP → BTH → AtomicETH → ICRC | 86B | Fetch-and-add atomic
RC ATOMIC_ACK | Eth → IPv4 → UDP → BTH → AETH → AtomicAckETH → ICRC | 70B | Atomic operation response

## Slide 8: UD (Unreliable Datagram) Packet Variants
Variant | Header Stack | Total Overhead | Use Case
UD SEND_ONLY | Eth → IPv4 → UDP → BTH → DETH → ICRC | 66B | Connectionless send
UD SEND_ONLY_IMM | Eth → IPv4 → UDP → BTH → DETH → ImmDt → ICRC | 70B | Connectionless send with immediate

## Slide 9: UC (Unreliable Connection) Packet Variants
Variant | Header Stack | Total Overhead | Use Case
UC SEND_ONLY | Eth → IPv4 → UDP → BTH → ICRC | 58B | Unreliable send
UC RDMA_WRITE_ONLY | Eth → IPv4 → UDP → BTH → RETH → ICRC | 74B | Unreliable RDMA write
UC RDMA_WRITE_FIRST | Eth → IPv4 → UDP → BTH → RETH → ICRC | 74B | First packet of unreliable write

## Slide 10: IPv6 Packet Variants (Add 20B to IPv4 overhead)
Variant | Header Stack | Total Overhead | Use Case
RC SEND_ONLY (IPv6) | Eth → IPv6 → UDP → BTH → ICRC | 78B | IPv6 single-packet send
RC RDMA_WRITE_ONLY (IPv6) | Eth → IPv6 → UDP → BTH → RETH → ICRC | 94B | IPv6 RDMA write
UD SEND_ONLY (IPv6) | Eth → IPv6 → UDP → BTH → DETH → ICRC | 86B | IPv6 connectionless send

## Slide 11: Header Overhead Summary
Detailed header size breakdown by component

## Slide 12: Header Size by Component (IPv4)
Operation | Eth | IP | UDP | BTH | Extended | ICRC | Total
SEND_ONLY | 14B | 20B | 8B | 12B | - | 4B | 58B
SEND_ONLY_IMM | 14B | 20B | 8B | 12B | 4B (ImmDt) | 4B | 62B
RDMA_WRITE_ONLY | 14B | 20B | 8B | 12B | 16B (RETH) | 4B | 74B
RDMA_WRITE_ONLY_IMM | 14B | 20B | 8B | 12B | 20B (RETH+ImmDt) | 4B | 78B
RDMA_READ_REQUEST | 14B | 20B | 8B | 12B | 16B (RETH) | 4B | 74B
RDMA_READ_RESPONSE | 14B | 20B | 8B | 12B | 4B (AETH) | 4B | 62B
ACK | 14B | 20B | 8B | 12B | 4B (AETH) | 4B | 62B
CMP_SWAP/FETCH_ADD | 14B | 20B | 8B | 12B | 28B (AtomicETH) | 4B | 86B
ATOMIC_ACK | 14B | 20B | 8B | 12B | 12B (AETH+AtomicAckETH) | 4B | 70B
UD SEND_ONLY | 14B | 20B | 8B | 12B | 8B (DETH) | 4B | 66B

## Slide 13: Protocol Efficiency Comparison (4KB Payload)
Protocol | Min Overhead | Max Overhead | Efficiency (4KB)
RoCEv2 RC SEND (IPv4) | 58B | 58B | 98.6%
RoCEv2 RC RDMA_WRITE (IPv4) | 74B | 74B | 98.2%
RoCEv2 UD SEND (IPv4) | 66B | 66B | 98.4%
RoCEv2 RC SEND (IPv6) | 78B | 78B | 98.1%
UE Standard | 100B | 100B | 97.6%
UE Small Message | 88B | 88B | 97.9%

## Slide 14: RoCEv2 RC SEND_ONLY Wire Format (58B)
┌──────────┬──────────┬──────────┬──────────┬──────────┐
│ Ethernet │ IPv4 │ UDP │ BTH │ ICRC │
│ 14B │ 20B │ 8B │ 12B │ 4B │
└──────────┴──────────┴──────────┴──────────┴──────────┘
Component Breakdown:
- Ethernet II (14B): dst_mac[6B], src_mac[6B], ethertype=0x0800[2B]
- IPv4 (20B): version, IHL, DSCP/ECN, length, ID, flags, TTL, protocol=17, checksum, src_ip, dst_ip
- UDP (8B): src_port (entropy), dst_port=4791, length, checksum
- BTH (12B): opcode=0x04, flags, p_key, dest_qp, ack_req, psn
- ICRC (4B): CRC-32 over BTH + payload (with masked fields)

## Slide 15: RoCEv2 RC RDMA_WRITE_ONLY Wire Format (74B)
┌──────────┬──────────┬──────────┬──────────┬──────────┬──────────┐
│ Ethernet │ IPv4 │ UDP │ BTH │ RETH │ ICRC │
│ 14B │ 20B │ 8B │ 12B │ 16B │ 4B │
└──────────┴──────────┴──────────┴──────────┴──────────┴──────────┘
RETH (16B):
- virtual_address[64b]: Remote memory address
- r_key[32b]: Remote key for memory authorization
- dma_length[32b]: Total bytes to transfer

## Slide 16: RoCEv2 RC CMP_SWAP/FETCH_ADD Wire Format (86B)
┌──────────┬──────────┬──────────┬──────────┬────────────┬──────────┐
│ Ethernet │ IPv4 │ UDP │ BTH │ AtomicETH │ ICRC │
│ 14B │ 20B │ 8B │ 12B │ 28B │ 4B │
└──────────┴──────────┴──────────┴──────────┴────────────┴──────────┘
AtomicETH (28B):
- virtual_address[64b]: Remote address (must be 8-byte aligned)
- r_key[32b]: Remote key for memory authorization
- swap_or_add_data[64b]: Swap value (CMP_SWAP) or Add value (FETCH_ADD)
- compare_data[64b]: Compare value (CMP_SWAP only, 0 for FETCH_ADD)
Semantics:
- CMP_SWAP: if (*addr == compare_data) { *addr = swap_data; } return original;
- FETCH_ADD: original = *addr; *addr += add_data; return original;

## Slide 17: Protocol Architecture
RoCEv2 Packet Encapsulation Stack

## Slide 18: RoCEv2 Protocol Stack

## Slide 19: Protocol Layer Sizes
Layer | Component | Size (bytes) | Notes
L2 | Ethernet II | 14 | +4 bytes if VLAN tagged
L3 | IPv4 | 20 | +options if present
L3 | IPv6 | 40 | +extension headers
L4 | UDP | 8 | Fixed size
Transport | BTH | 12 | Always present in RoCEv2
Trailer | ICRC | 4 | Always present

## Slide 20: Header Building Blocks
RoCEv2 Transport and Extended Headers

## Slide 21: RoCEv2 Header Datamodel Files
Header | File | Size | Purpose
BTH | bth.ksy | 12 bytes | Base Transport Header - present in all packets
RETH | reth.ksy | 16 bytes | RDMA Extended - remote address for RDMA ops
AETH | aeth.ksy | 4 bytes | ACK Extended - acknowledgment and credits
DETH | deth.ksy | 8 bytes | Datagram Extended - source QP for UD
ImmDt | immdt.ksy | 4 bytes | Immediate Data - 32-bit app-defined value
AtomicETH | atomiceth.ksy | 28 bytes | Atomic Extended - CMP_SWAP/FETCH_ADD
AtomicAckETH | atomicacketh.ksy | 8 bytes | Atomic ACK - original value response
ICRC | icrc.ksy | 4 bytes | Invariant CRC - end-to-end integrity
QP FSM | qp_state_machine.ksy | N/A | Queue Pair state machine definition

## Slide 22: Datamodel Location

## Slide 23: Base Transport Header (BTH)
12-byte header present in all RoCEv2 packets

## Slide 24: BTH Field Layout (bth.ksy)
Field | Bits | Offset | Description
opcode | 8 | 0 | Transport type [7:5] + Operation [4:0]
flags.SE | 1 | 1[7] | Solicited Event - request completion notification
flags.M | 1 | 1[6] | Migration state (MigReq)
flags.pad | 2 | 1[5:4] | Pad count (0-3 bytes)
flags.tver | 4 | 1[3:0] | Transport version (must be 0)
p_key | 16 | 2-3 | Partition key (bit 15 = membership type)
reserved | 8 | 4 | Reserved (FECN/BECN when ECN enabled)
dest_qp | 24 | 5-7 | Destination Queue Pair number
ack_req | 1 | 8[7] | ACK request (reliable transports only)
reserved2 | 7 | 8[6:0] | Reserved (must be zero)
psn | 24 | 9-11 | Packet Sequence Number (24-bit, wraps)

## Slide 25: BTH Opcode Encoding

## Slide 26: Packet Variant Matrix
Operations and Extended Headers by Type

## Slide 27: Operation Codes and Extended Headers (1/2)
Operation | Code | Extended Headers | Payload
SEND_FIRST | 0x00 | None | Yes
SEND_MIDDLE | 0x01 | None | Yes
SEND_LAST | 0x02 | None | Yes
SEND_LAST_IMM | 0x03 | ImmDt (4B) | Yes
SEND_ONLY | 0x04 | None | Yes
SEND_ONLY_IMM | 0x05 | ImmDt (4B) | Yes
RDMA_WRITE_FIRST | 0x06 | RETH (16B) | Yes
RDMA_WRITE_MIDDLE | 0x07 | None | Yes
RDMA_WRITE_LAST | 0x08 | None | Yes
RDMA_WRITE_LAST_IMM | 0x09 | ImmDt (4B) | Yes
RDMA_WRITE_ONLY | 0x0A | RETH (16B) | Yes
RDMA_WRITE_ONLY_IMM | 0x0B | RETH (16B) + ImmDt (4B) | Yes
RDMA_READ_REQUEST | 0x0C | RETH (16B) | No
RDMA_READ_RESP_FIRST | 0x0D | AETH (4B) | Yes
RDMA_READ_RESP_MIDDLE | 0x0E | None | Yes
RDMA_READ_RESP_LAST | 0x0F | AETH (4B) | Yes
RDMA_READ_RESP_ONLY | 0x10 | AETH (4B) | Yes
ACK | 0x11 | AETH (4B) | No

## Slide 28: Operation Codes and Extended Headers (2/2)
Operation | Code | Extended Headers | Payload
ATOMIC_ACK | 0x12 | AETH (4B) + AtomicAckETH (8B) | No
CMP_SWAP | 0x13 | AtomicETH (28B) | No
FETCH_ADD | 0x14 | AtomicETH (28B) | No

## Slide 29: RETH - RDMA Extended Transport Header
16-byte header for RDMA READ/WRITE operations

## Slide 30: RETH Field Layout (reth.ksy)
Field | Bits | Offset | Description
virtual_address | 64 | 0-7 | Remote virtual address for RDMA operation
r_key | 32 | 8-11 | Remote key for memory region authorization
dma_length | 32 | 12-15 | Total bytes to transfer (max 2GB)

## Slide 31: RETH Usage

## Slide 32: AETH - ACK Extended Transport Header
4-byte header for acknowledgments and responses

## Slide 33: AETH Field Layout (aeth.ksy)
Field | Bits | Offset | Description
syndrome | 8 | 0 | ACK type [6:5] + value [4:0]
msn | 24 | 1-3 | Message Sequence Number being acknowledged

## Slide 34: AETH Syndrome Encoding
Bits [6:5] | Type | Bits [4:0] Meaning
00 | ACK | Credit count (0-31, 31=unlimited)
01 | RNR NAK | RNR timeout value (encoded)
10 | Reserved | -
11 | NAK | NAK error code

## Slide 35: NAK Error Codes
Code | Name | Description
0x00 | PSN_SEQ_ERROR | PSN sequence error
0x01 | INVALID_REQUEST | Invalid request
0x02 | REMOTE_ACCESS_ERROR | Remote access error
0x03 | REMOTE_OP_ERROR | Remote operation error
0x04 | INVALID_RD_REQUEST | Invalid RD request

## Slide 36: AtomicETH - Atomic Extended Transport Header
28-byte header for atomic operations

## Slide 37: AtomicETH Field Layout (atomiceth.ksy)
Field | Bits | Offset | Description
virtual_address | 64 | 0-7 | Remote address (must be 8-byte aligned)
r_key | 32 | 8-11 | Remote key for memory authorization
swap_or_add_data | 64 | 12-19 | Swap value (CMP_SWAP) or Add value (FETCH_ADD)
compare_data | 64 | 20-27 | Compare value (CMP_SWAP only, 0 for FETCH_ADD)

## Slide 38: Atomic Operation Semantics

## Slide 39: QP State Machine
Queue Pair lifecycle from qp_state_machine.ksy

## Slide 40: QP States (IB Spec Section 10.3)
State | Description | Send | Receive
RESET | Initial state after QP creation | No | No
INIT | QP initialized, can post receive WQEs | No | Yes
RTR | Ready To Receive, remote QP configured | No | Yes
RTS | Ready To Send, fully operational | Yes | Yes
SQD | Send Queue Drained, graceful shutdown | Draining | Yes
SQE | Send Queue Error, recoverable | Halted | Yes
ERROR | Fatal error, must reset or destroy | No | No

## Slide 41: QP State Transitions

## Slide 42: Operation Validity Matrix
Operations supported by transport type

## Slide 43: Operation Validity by Transport Type
Operation | RC | UC | RD | UD | CNP
SEND_FIRST | Y | Y | Y | - | -
SEND_MIDDLE | Y | Y | Y | - | -
SEND_LAST | Y | Y | Y | - | -
SEND_LAST_IMM | Y | Y | Y | - | -
SEND_ONLY | Y | Y | Y | Y | -
SEND_ONLY_IMM | Y | Y | Y | Y | -
RDMA_WRITE_* | Y | Y | Y | - | -
RDMA_READ_* | Y | - | Y | - | -
ACK | Y | - | Y | - | -
ATOMIC_ACK | Y | - | Y | - | -
CMP_SWAP | Y | - | Y | - | -
FETCH_ADD | Y | - | Y | - | -

## Slide 44: Transport Type Restrictions

## Slide 45: Header Overhead Summary
Total header sizes by operation type

## Slide 46: Header Overhead by Operation
Operation | BTH | Extended | ICRC | Min Total
SEND_ONLY | 12 | 0 | 4 | 16 bytes
SEND_ONLY_IMM | 12 | 4 (ImmDt) | 4 | 20 bytes
RDMA_WRITE_ONLY | 12 | 16 (RETH) | 4 | 32 bytes
RDMA_WRITE_ONLY_IMM | 12 | 20 (RETH+ImmDt) | 4 | 36 bytes
RDMA_READ_REQUEST | 12 | 16 (RETH) | 4 | 32 bytes
RDMA_READ_RESPONSE | 12 | 4 (AETH) | 4 | 20 bytes
ACK | 12 | 4 (AETH) | 4 | 20 bytes
CMP_SWAP | 12 | 28 (AtomicETH) | 4 | 44 bytes
FETCH_ADD | 12 | 28 (AtomicETH) | 4 | 44 bytes
ATOMIC_ACK | 12 | 12 (AETH+AtomicAckETH) | 4 | 28 bytes
UD SEND_ONLY | 12 | 8 (DETH) | 4 | 24 bytes

## Slide 47: ICRC - Invariant CRC
End-to-end integrity from icrc.ksy

## Slide 48: ICRC Parameters
Parameter | Value | Description
Polynomial | 0x04C11DB7 | CRC-32 (IEEE 802.3)
Polynomial (reflected) | 0xEDB88320 | For table-driven implementation
Initial value | 0xFFFFFFFF | All 1s
Final XOR | 0xFFFFFFFF | Inverts result
Seed (RoCEv2) | 0xDEBB20E3 | Pre-computed for masked LRH

## Slide 49: ICRC Coverage and Masking

## Slide 50: Datamodel Coverage
Complete RoCE KSY file inventory

## Slide 51: RoCE Datamodel Files (9 total)
Category | File | Path | IB Spec Section
Transport | bth.ksy | roce/transport/bth.ksy | Section 9.2
Transport | reth.ksy | roce/transport/reth.ksy | Section 9.3
Transport | aeth.ksy | roce/transport/aeth.ksy | Section 9.4
Transport | deth.ksy | roce/transport/deth.ksy | Section 9.5
Transport | immdt.ksy | roce/transport/immdt.ksy | Section 9.6
Transport | atomiceth.ksy | roce/transport/atomiceth.ksy | Section 9.8
Transport | atomicacketh.ksy | roce/transport/atomicacketh.ksy | Section 9.9
Transport | icrc.ksy | roce/transport/icrc.ksy | Section 9.7
Protocol | qp_state_machine.ksy | roce/protocols/qp_state_machine.ksy | Section 10.3

## Slide 52: Datamodel Features

## Slide 53: Detailed Header Formats
Field-level documentation with packet diagrams

## Slide 54: RoCEv2 Base Transport Header
12 bytes (96 bits)

## Slide 55: roce_bth Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| opcode | flags | pkey |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| reserved | dest_qp |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|a| reserved2 | psn |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 56: roce_bth Field Definitions
Field | Bits | Offset | Type | Description
opcode | 8 | 0 | u1 | Operation code (8 bits)
flags | 8 | 8 | u1 | Flags byte containing:
pkey | 16 | 16 | u2 | Partition Key (16 bits)
reserved | 8 | 32 | b8 | Reserved field (8 bits).
dest_qp | 24 | 40 | b24 | Destination Queue Pair number (24 bits)
ack_req | 1 | 64 | b1 | Acknowledge Request (1 bit)
reserved2 | 7 | 65 | b7 | Reserved field (7 bits, must be zero)
psn | 24 | 72 | b24 | Packet Sequence Number (24 bits)

## Slide 57: RoCEv2 RDMA Extended Transport Header
16 bytes (128 bits)

## Slide 58: roce_reth Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| virtual_address |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| virtual_address |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| rkey |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dma_length |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 59: roce_reth Field Definitions
Field | Bits | Offset | Type | Description
virtual_address | 64 | 0 | u8 | Virtual Address (64 bits)
rkey | 32 | 64 | u4 | Remote Key (32 bits)
dma_length | 32 | 96 | u4 | DMA Length (32 bits)

## Slide 60: RoCEv2 ACK Extended Transport Header
4 bytes (32 bits)

## Slide 61: roce_aeth Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| syndrome | msn |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 62: roce_aeth Field Definitions
Field | Bits | Offset | Type | Description
syndrome | 8 | 0 | u1 | Syndrome field (8 bits) - per IB Spec Vol 1, v1.4, Table 46
msn | 24 | 8 | b24 | Message Sequence Number (24 bits)

## Slide 63: RoCEv2 Datagram Extended Transport Header
8 bytes (64 bits)

## Slide 64: roce_deth Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| qkey |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| reserved | src_qp |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 65: roce_deth Field Definitions
Field | Bits | Offset | Type | Description
qkey | 32 | 0 | u4 | Queue Key (32 bits)
reserved | 8 | 32 | b8 | Reserved field (8 bits, must be zero)
src_qp | 24 | 40 | b24 | Source Queue Pair number (24 bits)

## Slide 66: RoCEv2 Atomic Extended Transport Header
28 bytes (224 bits)

## Slide 67: roce_atomiceth Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| virtual_address |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| virtual_address |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| rkey |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| swap_or_add_data |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| swap_or_add_data |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| compare_data |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| compare_data |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 68: roce_atomiceth Field Definitions
Field | Bits | Offset | Type | Description
virtual_address | 64 | 0 | u8 | Virtual Address (64 bits)
rkey | 32 | 64 | u4 | Remote Key (32 bits)
swap_or_add_data | 64 | 96 | u8 | Swap/Add Data (64 bits)
compare_data | 64 | 160 | u8 | Compare Data (64 bits)

## Slide 69: RoCEv2 Immediate Data
4 bytes (32 bits)

## Slide 70: roce_immdt Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| immediate_data |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 71: roce_immdt Field Definitions
Field | Bits | Offset | Type | Description
immediate_data | 32 | 0 | u4 | Immediate Data value (32 bits)

## Slide 72: References
Specification and Documentation Sources

## Slide 73: Primary References

## Slide 74: Internal Documentation