## Slide 1: PMR Packet Taxonomy: Ethernet Technical Report
IEEE 802.3 and IP Protocol Formats
Packet Taxonomy Team
Cornelis Networks Engineering

## Slide 2: Table of Contents
Overview
Protocol Architecture
Header Building Blocks
Packet Variant Matrix
Detailed Packet Structures
RSS Hash Algorithm
Header Overhead Summary
Datamodel Coverage
Detailed Header Formats
Ethernet II Frame
IEEE 802.1Q VLAN Tag
IEEE 802.2 LLC Header
SNAP Extension Header
IPv6 Header
UDP Header
IEEE 802.3 MAC Frame
IPv4 Header
TCP Header
References

## Slide 3: Overview
Standard Ethernet Protocol Stack

## Slide 4: Ethernet Protocol Coverage

## Slide 5: PMR Use Cases

## Slide 6: Protocol Architecture
OSI Layer Mapping

## Slide 7: OSI Layer to Datamodel Mapping
OSI Layer | Protocol | KSY File | Size (bytes)
Layer 2 (Link) | Ethernet II | link/ethernet_ii.ksy | 14
Layer 2 (Link) | IEEE 802.3 | link/ethernet_802_3.ksy | 14
Layer 2 (Link) | VLAN 802.1Q | link/vlan_802_1q.ksy | 4
Layer 2 (Link) | LLC | link/llc.ksy | 3-4
Layer 2 (Link) | SNAP | link/snap.ksy | 5
Layer 3 (Network) | IPv4 | network/ipv4.ksy | 20-60
Layer 3 (Network) | IPv6 | network/ipv6.ksy | 40
Layer 4 (Transport) | TCP | transport/tcp.ksy | 20-60
Layer 4 (Transport) | UDP | transport/udp.ksy | 8
Offload | RSS Hash Algorithm | rss/hash_algorithm.ksy | 4
Offload | RSS Toeplitz Key | rss/toeplitz_key.ksy | 40
Offload | RSS Hash Input | rss/hash_input.ksy | 8-36

## Slide 8: Header Building Blocks
All 12 Ethernet KSY Files

## Slide 9: Link Layer Headers (5 files)
File | Protocol | Size | Spec Reference
ethernet_ii.ksy | Ethernet II (DIX) | 14 bytes | IEEE 802.3-2022 Section 3.1.1
ethernet_802_3.ksy | IEEE 802.3 MAC Frame | 14 bytes | IEEE 802.3-2022 Section 3.1.1
vlan_802_1q.ksy | VLAN Tag (802.1Q) | 4 bytes | IEEE 802.1Q-2022 Section 9
llc.ksy | LLC Header (802.2) | 3-4 bytes | IEEE 802.2 / ISO 8802-2
snap.ksy | SNAP Extension | 5 bytes | IEEE 802 / RFC 1042

## Slide 10: Network Layer Headers (2 files)
File | Protocol | Size | Spec Reference
ipv4.ksy | IPv4 Header | 20-60 bytes | RFC 791 Section 3.1
ipv6.ksy | IPv6 Header | 40 bytes | RFC 8200 Section 3

## Slide 11: Transport Layer Headers (2 files)
File | Protocol | Size | Spec Reference
tcp.ksy | TCP Header | 20-60 bytes | RFC 793 Section 3.1
udp.ksy | UDP Header | 8 bytes | RFC 768

## Slide 12: RSS Offload Configuration (3 files)
File | Purpose | Size | CSR Reference
hash_algorithm.ksy | Algorithm Selection | 4 bytes | rx_classify.pdp_hash_cfg @ 0x3014
toeplitz_key.ksy | Toeplitz Hash Key | 40 bytes | ethernet.rss_hash_key[0-9] @ 0x4010-0x4034
hash_input.ksy | Hash Input Formats | 8-36 bytes | N/A (data format)

## Slide 13: Packet Variant Matrix
Frame Types and Encapsulations

## Slide 14: Ethernet Frame Types
Frame Type | Discriminator | Header Stack | Use Case
Ethernet II | EtherType >= 0x0600 | Eth II + IP + TCP/UDP | Standard data traffic
IEEE 802.3 | Length < 0x0600 | 802.3 + LLC + [SNAP] | Control protocols (STP, CDP)
VLAN Tagged | EtherType = 0x8100 | Eth II + VLAN + IP | Network segmentation
QinQ | EtherType = 0x88A8 | Eth II + VLAN + VLAN + IP | Provider bridging

## Slide 15: Common EtherType Values
EtherType | Protocol | Next Header
0x0800 | IPv4 | network/ipv4.ksy
0x86DD | IPv6 | network/ipv6.ksy
0x8100 | VLAN 802.1Q | link/vlan_802_1q.ksy
0x88A8 | QinQ (802.1ad) | link/vlan_802_1q.ksy
0x0806 | ARP | N/A

## Slide 16: IP Protocol Numbers
Protocol | Value | Next Header
TCP | 6 | transport/tcp.ksy
UDP | 17 | transport/udp.ksy
ICMP | 1 | N/A
ICMPv6 | 58 | N/A

## Slide 17: Detailed Packet Structures
Wire Format Specifications

## Slide 18: Ethernet II Header (14 bytes) - ethernet_ii.ksy
Field | Bits | Offset | Description
dst_mac | 48 | 0-5 | Destination MAC address
src_mac | 48 | 6-11 | Source MAC address
ether_type | 16 | 12-13 | Protocol type (>= 0x0600)

## Slide 19: VLAN 802.1Q Tag (4 bytes) - vlan_802_1q.ksy
Field | Bits | Offset | Description
tpid | 16 | 0-1 | Tag Protocol ID (0x8100)
pcp | 3 | 2[7:5] | Priority Code Point (0-7)
dei | 1 | 2[4] | Drop Eligible Indicator
vid | 12 | 2[3:0],3 | VLAN Identifier (0-4095)

## Slide 20: IPv4 Header (20-60 bytes) - ipv4.ksy
Field | Bits | Offset | Description
version | 4 | 0[7:4] | IP version (4)
ihl | 4 | 0[3:0] | Header length (words)
dscp | 6 | 1[7:2] | Differentiated Services
ecn | 2 | 1[1:0] | ECN bits
total_length | 16 | 2-3 | Total packet length
identification | 16 | 4-5 | Fragment ID
flags | 3 | 6[7:5] | DF, MF flags
frag_offset | 13 | 6[4:0],7 | Fragment offset
ttl | 8 | 8 | Time to live
protocol | 8 | 9 | Next protocol
checksum | 16 | 10-11 | Header checksum
src_ip | 32 | 12-15 | Source IP address
dst_ip | 32 | 16-19 | Destination IP address

## Slide 21: IPv6 Header (40 bytes) - ipv6.ksy
Field | Bits | Offset | Description
version | 4 | 0[7:4] | IP version (6)
traffic_class | 8 | 0[3:0],1[7:4] | Traffic class (DSCP+ECN)
flow_label | 20 | 1[3:0],2-3 | Flow label
payload_length | 16 | 4-5 | Payload length
next_header | 8 | 6 | Next header type
hop_limit | 8 | 7 | Hop limit (TTL)
src_addr | 128 | 8-23 | Source address
dst_addr | 128 | 24-39 | Destination address

## Slide 22: TCP Header (20-60 bytes) - tcp.ksy
Field | Bits | Offset | Description
src_port | 16 | 0-1 | Source port
dst_port | 16 | 2-3 | Destination port
seq_num | 32 | 4-7 | Sequence number
ack_num | 32 | 8-11 | Acknowledgment number
data_offset | 4 | 12[7:4] | Header length (words)
reserved | 3 | 12[3:1] | Reserved
flags | 9 | 12[0],13 | TCP flags (NS,CWR,ECE,URG,ACK,PSH,RST,SYN,FIN)
window | 16 | 14-15 | Window size
checksum | 16 | 16-17 | TCP checksum
urgent_ptr | 16 | 18-19 | Urgent pointer

## Slide 23: UDP Header (8 bytes) - udp.ksy
Field | Bits | Offset | Description
src_port | 16 | 0-1 | Source port
dst_port | 16 | 2-3 | Destination port
length | 16 | 4-5 | UDP length
checksum | 16 | 6-7 | UDP checksum

## Slide 24: RSS Hash Algorithm
Receive Side Scaling Configuration

## Slide 25: Hash Algorithm Selection - hash_algorithm.ksy
Value | Algorithm | Key Required | Use Case
0 | CRC32 | No | Default at reset, good distribution
1 | XOR | No | Testing/debugging only, poor distribution
2 | Toeplitz | Yes (40 bytes) | Production, per Microsoft RSS spec

## Slide 26: Hash Input Formats - hash_input.ksy
Hash Type | Input Size | Fields | Min Key Size
IPv4 L3 | 8 bytes | src_ip (4) + dst_ip (4) | 12 bytes
IPv4 L4 | 12 bytes | src_ip (4) + dst_ip (4) + ports (4) | 16 bytes
IPv6 L3 | 32 bytes | src_ip (16) + dst_ip (16) | 36 bytes
IPv6 L4 | 36 bytes | src_ip (16) + dst_ip (16) + ports (4) | 40 bytes

## Slide 27: Toeplitz Key CSR Layout - toeplitz_key.ksy
Register | Offset | Key Bytes
rss_hash_key[0] | 0x4010 | 0-3
rss_hash_key[1] | 0x4014 | 4-7
rss_hash_key[2] | 0x4018 | 8-11
rss_hash_key[3] | 0x401C | 12-15
rss_hash_key[4] | 0x4020 | 16-19
rss_hash_key[5] | 0x4024 | 20-23
rss_hash_key[6] | 0x4028 | 24-27
rss_hash_key[7] | 0x402C | 28-31
rss_hash_key[8] | 0x4030 | 32-35
rss_hash_key[9] | 0x4034 | 36-39

## Slide 28: Toeplitz Algorithm

## Slide 29: Header Overhead Summary
Encapsulation Costs

## Slide 30: Common Packet Configurations
Configuration | Headers | Total Overhead
IPv4/TCP (no VLAN) | Eth II (14) + IPv4 (20) + TCP (20) | 54 bytes
IPv4/UDP (no VLAN) | Eth II (14) + IPv4 (20) + UDP (8) | 42 bytes
IPv4/TCP (VLAN) | Eth II (14) + VLAN (4) + IPv4 (20) + TCP (20) | 58 bytes
IPv6/TCP (no VLAN) | Eth II (14) + IPv6 (40) + TCP (20) | 74 bytes
IPv6/UDP (no VLAN) | Eth II (14) + IPv6 (40) + UDP (8) | 62 bytes
IPv6/TCP (VLAN) | Eth II (14) + VLAN (4) + IPv6 (40) + TCP (20) | 78 bytes
802.3/LLC/SNAP/IPv4 | 802.3 (14) + LLC (3) + SNAP (5) + IPv4 (20) | 42 bytes

## Slide 31: Maximum Header Sizes
Header | Minimum | Maximum | Variable Component
Ethernet II | 14 bytes | 14 bytes | Fixed
VLAN 802.1Q | 4 bytes | 4 bytes | Fixed
LLC | 3 bytes | 4 bytes | Control field format
IPv4 | 20 bytes | 60 bytes | Options (0-40 bytes)
IPv6 | 40 bytes | 40 bytes | Fixed (extensions separate)
TCP | 20 bytes | 60 bytes | Options (0-40 bytes)
UDP | 8 bytes | 8 bytes | Fixed

## Slide 32: Datamodel Coverage
All 12 Ethernet KSY Files

## Slide 33: Complete KSY File Inventory
Category | File Path | Protocol | Lines
Link | link/ethernet_ii.ksy | Ethernet II (DIX) | 138
Link | link/ethernet_802_3.ksy | IEEE 802.3 MAC | 99
Link | link/vlan_802_1q.ksy | VLAN 802.1Q | 148
Link | link/llc.ksy | LLC (802.2) | 176
Link | link/snap.ksy | SNAP Extension | 108
Network | network/ipv4.ksy | IPv4 | 219
Network | network/ipv6.ksy | IPv6 | 191
Transport | transport/tcp.ksy | TCP | 199
Transport | transport/udp.ksy | UDP | 137
RSS | rss/hash_algorithm.ksy | Hash Algorithm | 146
RSS | rss/toeplitz_key.ksy | Toeplitz Key | 216
RSS | rss/hash_input.ksy | Hash Input Formats | 228

## Slide 34: Datamodel Features

## Slide 35: Detailed Header Formats
Field-level documentation with packet diagrams

## Slide 36: Ethernet II Frame
14 bytes (112 bits)

## Slide 37: ethernet_ii Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dst_mac |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dst_mac | src_mac |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| src_mac |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| ether_type |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 38: ethernet_ii Field Definitions
Field | Bits | Offset | Type | Description
dst_mac | 48 | 0 |  | Destination MAC address (6 bytes)
src_mac | 48 | 48 |  | Source MAC address (6 bytes)
ether_type | 16 | 96 | u2 | EtherType field (2 bytes, big-endian)
payload | 0 | 112 |  | Frame payload (variable length)

## Slide 39: IEEE 802.1Q VLAN Tag
4 bytes (32 bits)

## Slide 40: vlan_802_1q Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| tpid | tci |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| ether_type |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 41: vlan_802_1q Field Definitions
Field | Bits | Offset | Type | Description
tpid | 16 | 0 | u2 | Tag Protocol Identifier (TPID)
tci | 16 | 16 | u2 | Tag Control Information (PCP + DEI + VID)
ether_type | 16 | 32 | u2 | EtherType of encapsulated payload

## Slide 42: IEEE 802.2 LLC Header
4 bytes (32 bits)

## Slide 43: llc Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dsap | ssap | control | control_ext |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 44: llc Field Definitions
Field | Bits | Offset | Type | Description
dsap | 8 | 0 | u1 | Destination Service Access Point
ssap | 8 | 8 | u1 | Source Service Access Point
control | 8 | 16 | u1 | Control field (first byte).
control_ext | 8 | 24 | u1 | Extended control field (second byte for I/S-format)

## Slide 45: SNAP Extension Header
5 bytes (40 bits)

## Slide 46: snap Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| oui | protocol_id |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| protocol_id |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 47: snap Field Definitions
Field | Bits | Offset | Type | Description
oui | 24 | 0 |  | Organizationally Unique Identifier (3 bytes).
protocol_id | 16 | 24 | u2 | Protocol identifier (2 bytes).

## Slide 48: IPv6 Header
40 bytes (320 bits)

## Slide 49: ipv6 Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| version_tc_fl |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| payload_length | next_header | hop_limit |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| src_addr |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| src_addr |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| src_addr |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| src_addr |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dst_addr |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dst_addr |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dst_addr |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dst_addr |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 50: ipv6 Field Definitions
Field | Bits | Offset | Type | Description
version_tc_fl | 32 | 0 | u4 | Version (4 bits) + Traffic Class (8 bits) + Flow Label (20 b
payload_length | 16 | 32 | u2 | Payload length (excludes 40-byte fixed header)
next_header | 8 | 48 | u1 | Next header type (same values as IPv4 protocol field)
hop_limit | 8 | 56 | u1 | Hop limit (equivalent to IPv4 TTL)
src_addr | 128 | 64 |  | Source IPv6 address (128 bits)
dst_addr | 128 | 192 |  | Destination IPv6 address (128 bits)

## Slide 51: UDP Header
8 bytes (64 bits)

## Slide 52: udp Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| src_port | dst_port |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| length | checksum |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 53: udp Field Definitions
Field | Bits | Offset | Type | Description
src_port | 16 | 0 | u2 | Source port number (0-65535)
dst_port | 16 | 16 | u2 | Destination port number (0-65535)
length | 16 | 32 | u2 | Total length including header (minimum 8)
checksum | 16 | 48 | u2 | UDP checksum (optional in IPv4, mandatory in IPv6)

## Slide 54: IEEE 802.3 MAC Frame
14 bytes (112 bits)

## Slide 55: ethernet_802_3 Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dst_mac |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dst_mac | src_mac |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| src_mac |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| length |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 56: ethernet_802_3 Field Definitions
Field | Bits | Offset | Type | Description
dst_mac | 48 | 0 |  | Destination MAC address (6 bytes)
src_mac | 48 | 48 |  | Source MAC address (6 bytes)
length | 16 | 96 | u2 | Length of LLC data in bytes (must be < 0x0600).
llc_data | 0 | 112 |  | LLC header and payload (variable length per length field)

## Slide 57: IPv4 Header
20 bytes (160 bits)

## Slide 58: ipv4 Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| version_ihl | dscp_ecn | total_length |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| identification | flags_fragment_offset |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| ttl | protocol | header_checksum |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| src_addr |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| dst_addr |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 59: ipv4 Field Definitions
Field | Bits | Offset | Type | Description
version_ihl | 8 | 0 | u1 | Version (4 bits) + Internet Header Length (4 bits)
dscp_ecn | 8 | 8 | u1 | DSCP (6 bits) + ECN (2 bits)
total_length | 16 | 16 | u2 | Total packet length including header and data
identification | 16 | 32 | u2 | Fragment identification
flags_fragment_offset | 16 | 48 | u2 | Flags (3 bits) + Fragment Offset (13 bits)
ttl | 8 | 64 | u1 | Time To Live (hop limit)
protocol | 8 | 72 | u1 | Upper layer protocol (6=TCP, 17=UDP, 1=ICMP)
header_checksum | 16 | 80 | u2 | Header checksum (ones' complement)
src_addr | 32 | 96 | u4 | Source IP address
dst_addr | 32 | 128 | u4 | Destination IP address
options | 0 | 160 |  | IP options (variable length, if IHL > 5)

## Slide 60: TCP Header
20 bytes (160 bits)

## Slide 61: tcp Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| src_port | dst_port |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| seq_num |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| ack_num |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| data_offset_reserved_flags | window_size |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| checksum | urgent_pointer |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 62: tcp Field Definitions
Field | Bits | Offset | Type | Description
src_port | 16 | 0 | u2 | Source port number (0-65535)
dst_port | 16 | 16 | u2 | Destination port number (0-65535)
seq_num | 32 | 32 | u4 | Sequence number
ack_num | 32 | 64 | u4 | Acknowledgment number (if ACK flag set)
data_offset_reserved_flags | 16 | 96 | u2 | Data offset (4 bits) + Reserved (3 bits) + Flags (9 bits)
window_size | 16 | 112 | u2 | Window size (receive window)
checksum | 16 | 128 | u2 | TCP checksum (pseudo-header + header + data)
urgent_pointer | 16 | 144 | u2 | Urgent pointer (if URG flag set)
options | 0 | 160 |  | TCP options (variable length)

## Slide 63: References
Standards and Specifications

## Slide 64: IEEE Standards
Standard | Title | KSY Files
IEEE 802.3-2022 | Ethernet Standard | ethernet_ii.ksy, ethernet_802_3.ksy
IEEE 802.1Q-2022 | VLAN Bridging | vlan_802_1q.ksy
IEEE 802.2 | Logical Link Control | llc.ksy

## Slide 65: IETF RFCs
RFC | Title | KSY Files
RFC 791 | Internet Protocol (IPv4) | ipv4.ksy
RFC 8200 | Internet Protocol Version 6 (IPv6) | ipv6.ksy
RFC 793 | Transmission Control Protocol (TCP) | tcp.ksy
RFC 768 | User Datagram Protocol (UDP) | udp.ksy
RFC 1042 | IP over IEEE 802 Networks | snap.ksy
RFC 2474 | Differentiated Services (DSCP) | ipv4.ksy, ipv6.ksy
RFC 3168 | Explicit Congestion Notification (ECN) | ipv4.ksy, ipv6.ksy, tcp.ksy

## Slide 66: Other References
Reference | Description | KSY Files
Microsoft RSS Specification | Receive Side Scaling | hash_algorithm.ksy, toeplitz_key.ksy, hash_input.ksy
NDIS Documentation | Network Driver Interface | hash_algorithm.ksy, toeplitz_key.ksy

## Slide 67: Analysis Document