## Slide 1: PMR Packet Taxonomy: Ultra Ethernet Technical Report
UE Specification v1.0.1 Protocol Formats
Packet Taxonomy Team
Cornelis Networks Engineering

## Slide 2: Table of Contents
Ultra Ethernet Overview
UE Packet Variants
Header Overhead Summary
Protocol Architecture
UE Protocol Enumerations
UE Protocol State Machines
PDS Header Building Blocks
SES Header Building Blocks
CMS Header Building Blocks
TSS Header Building Blocks
Link Layer Building Blocks
Network and Physical Layer
PDS Packet Variant Matrix
SES Packet Variant Matrix
Detailed Packet Structures
State Machines Summary
Header Overhead Summary
Complete Datamodel Coverage
Detailed Header Formats
LLR Preamble 64B/66B Block Format
LLR_ACK Control Ordered Set (CtlOS)
LLR_NACK Control Ordered Set (CtlOS)
CBFC CF_Update Control Ordered Set (CtlOS)
CBFC CC_Update Message
UE Link Negotiation Options TLV
UE CBFC TLV
References

## Slide 3: Ultra Ethernet Overview
Protocol Architecture and Key Characteristics

## Slide 4: UE Protocol Key Characteristics
• High-performance RDMA transport over Ethernet infrastructure
• Layered architecture: Physical, Link, Network, Transport
• Transport sublayers: PDS (Packet Delivery), SES (Semantic), CMS (Congestion), TSS (Security)
• Multiple delivery modes: RUD, ROD, RUDI, UUD
• Congestion control algorithms: NSCC, RCCC, TFC
• Link-layer reliability via LLR (Link Layer Reliable)
• Credit-based flow control via CBFC
• AES-GCM encryption via TSS

## Slide 5: UE Datamodel Coverage Summary
Layer | Sublayer | Format Files | Protocol Files | Total
Transport | PDS | 14 | 16 | 30
Transport | SES | 15 | 12 | 27
Transport | CMS | 7 | 8 | 15
Transport | TSS | 2 | 7 | 9
Link | LLR | 6 | 3 | 9
Link | LLDP | 2 | 1 | 3
Link | CBFC | 2 | 3 | 5
Network | - | 4 | 0 | 4
Physical | - | 1 | 0 | 1
**Total** | - | **53** | **50** | **103**

## Slide 6: UE Packet Variants
Complete packet type matrix with header stacks

## Slide 7: Basic UE Packets (No Encryption)
Variant | Header Stack | Total Overhead | Use Case
UE Standard | Eth → IPv4 → UDP → PDS → SES(std) | 100B | Standard tagged send/recv
UE Small Message | Eth → IPv4 → UDP → PDS → SES(small) | 88B | Small messages (<256B)
UE + CSIG Compact | Eth → IPv4 → UDP → PDS → CC(8B) → SES | 108B | Standard + NSCC congestion state
UE + CSIG Wide | Eth → IPv4 → UDP → PDS → CC(16B) → SES | 116B | Standard + extended CC state
UE Rendezvous | Eth → IPv4 → UDP → PDS → SES(std) → RDV(32B) | 132B | Large message transfers
UE Deferrable | Eth → IPv4 → UDP → PDS → SES(defer) | 100B | CCL-style unexpected messaging

## Slide 8: UE IPv4 Native Packets (No UDP)
Variant | Header Stack | Total Overhead | Use Case
UE IPv4 Native | Eth → IPv4 → Entropy → PDS → SES(std) | 96B | 4B savings vs UDP
UE IPv4 + CSIG Compact | Eth → IPv4 → Entropy → PDS → CC(8B) → SES | 104B | Native + congestion state
UE IPv4 + CSIG Wide | Eth → IPv4 → Entropy → PDS → CC(16B) → SES | 112B | Native + extended CC

## Slide 9: Encrypted UE Packets (TSS)
Variant | Header Stack | Total Overhead | Use Case
UE Encrypted | Eth → IPv4 → UDP → TSS → PDS → SES | 112B + 16B auth | Secure domain traffic
UE Encrypted Small | Eth → IPv4 → UDP → TSS → PDS → SES(small) | 100B + 16B auth | Secure small messages
UE IPv4 Encrypted | Eth → IPv4 → Entropy → TSS → PDS → SES | 108B + 16B auth | Secure native IPv4

## Slide 10: Header Overhead Summary
Detailed header size breakdown by component

## Slide 11: Header Size by Component
Variant | Eth | IP | UDP/Ent | TSS | PDS | CC | SES | Total | Auth
UE Standard | 14B | 20B | 8B | - | 14B | - | 44B | 100B | -
UE Small | 14B | 20B | 8B | - | 14B | - | 32B | 88B | -
UE + CSIG Compact | 14B | 20B | 8B | - | 14B | 8B | 44B | 108B | -
UE + CSIG Wide | 14B | 20B | 8B | - | 14B | 16B | 44B | 116B | -
UE IPv4 Native | 14B | 20B | 4B | - | 14B | - | 44B | 96B | -
UE Encrypted | 14B | 20B | 8B | 12B | 14B | - | 44B | 112B | 16B
UE Rendezvous | 14B | 20B | 8B | - | 14B | - | 76B | 132B | -

## Slide 12: Protocol Efficiency Comparison (4KB Payload)
Protocol | Min Overhead | Max Overhead | Efficiency (4KB)
UE Standard | 100B | 100B | 97.6%
UE Small Message | 88B | 88B | 97.9%
UE IPv4 Native | 96B | 96B | 97.7%
UE Encrypted | 128B | 128B | 96.9%
RoCEv2 (IPv4) | 58B | 78B | 98.6%
RoCEv2 (IPv6) | 78B | 98B | 98.1%

## Slide 13: UE Standard Tagged Send Wire Format (100B)
┌──────────┬──────────┬──────────┬──────────────┬──────────────┬──────────┬──────────┐
│ Ethernet │ IPv4 │ UDP │ PDS Prologue │ PDS RUD/ROD │ SES Std │ Data │
│ 14B │ 20B │ 8B │ 2B │ 12B │ 44B │ Variable │
└──────────┴──────────┴──────────┴──────────────┴──────────────┴──────────┴──────────┘
Component Breakdown:
- Ethernet II (14B): dst_mac[6B], src_mac[6B], ethertype=0x0800[2B]
- IPv4 (20B): version, IHL, TOS, length, ID, flags, TTL, protocol=17, checksum, src_ip, dst_ip
- UDP (8B): src_port (entropy), dst_port=4791, length, checksum
- PDS Prologue (2B): type[5b], next_hdr[4b], flags[7b]
- PDS RUD Request (12B): psn[24b], spdcid[24b], dpdcid[24b], clear_psn_offset[24b]
- SES Standard SOM=1 (44B): opcode, flags, match_bits, initiator, buffer_offset, rkey, context

## Slide 14: UE Small Message Wire Format (88B)
┌──────────┬──────────┬──────────┬──────────────┬──────────────┬──────────────┬──────────┐
│ Ethernet │ IPv4 │ UDP │ PDS Prologue │ PDS RUD/ROD │ SES Small │ Data │
│ 14B │ 20B │ 8B │ 2B │ 12B │ 32B │ Variable │
└──────────┴──────────┴──────────┴──────────────┴──────────────┴──────────────┴──────────┘
SES Small Message (32B):
- opcode[6b] + version[2b]: Operation code (0x08 for small message)
- flags[8b]: dc, ie, rel, hd, eom=1, som=1
- request_length[14b]: Max 16383 bytes
- ri_generation[8b], job_id[24b], pid_on_fep[12b], resource_index[12b]
- initiator[32b], match_bits[64b], header_data[64b]
Constraints: Single-packet only (som=1, eom=1), max payload 16383B

## Slide 15: UE Encrypted Packet Wire Format (112B + 16B auth)
┌──────────┬──────────┬──────────┬──────────────┬──────────┬──────────────┬──────────┬──────────┬──────────┐
│ Ethernet │ IPv4 │ UDP │ PDS Prologue │ TSS │ PDS RUD/ROD │ SES Std │ Data │ Auth Tag │
│ 14B │ 20B │ 8B │ 2B │ 12B │ 12B │ 44B │ Variable │ 16B │
└──────────┴──────────┴──────────┴──────────────┴──────────┴──────────────┴──────────┴──────────┴──────────┘
│◄────────────── Encrypted ──────────────►│
│◄─────────────────────── Authenticated ──────────────────────►│
TSS Header (12B):
- tss_type[4b]: TSS packet type
- tss_flags[4b]: TSS flags
- security_context_id[32b]: Security association identifier
- sequence_number[32b]: Anti-replay sequence number
- reserved[24b]
Encryption: AES-GCM with 16-byte authentication tag

## Slide 16: Protocol Architecture
UE Layer Diagram and Sublayer Relationships

## Slide 17: UE Protocol Stack (text)
+------------------------------------------------------------------+
| Application / RDMA Verbs |
+------------------------------------------------------------------+
| |
| TRANSPORT LAYER |
| +-------------------------------------------------------------+ |
| | SES (Semantic Sublayer) | |
| | - Request/Response operations | |
| | - RDMA Read/Write, Atomics, Tagged Send | |
| +-------------------------------------------------------------+ |
| | PDS (Packet Delivery Sublayer) | |
| | - Reliable/Unreliable delivery | |
| | - Sequence numbers, ACK/NACK | |
| +-------------------------------------------------------------+ |
| | CMS (Congestion Management Sublayer) | |
| | - NSCC, RCCC, TFC algorithms | |
| +-------------------------------------------------------------+ |
| | TSS (Transport Security Sublayer) | |
| | - AES-GCM encryption | |
| +-------------------------------------------------------------+ |
| |
+------------------------------------------------------------------+
| NETWORK LAYER |
| - IPv4/IPv6 encapsulation |
| - DSCP categories, packet trimming |
+------------------------------------------------------------------+
| LINK LAYER |
| +-------------------------------------------------------------+ |
| | LLR (Link Layer Reliable) | |
| | - Hop-by-hop reliability | |
| +-------------------------------------------------------------+ |
| | CBFC (Credit-Based Flow Control) | |
| | - Per-VC flow control | |
| +-------------------------------------------------------------+ |
+------------------------------------------------------------------+
| PHYSICAL LAYER |
| - 64B/66B encoding, Control Ordered Sets |
+------------------------------------------------------------------+

## Slide 18: UE Protocol Enumerations
Value definitions extracted from KSY datamodel files

## Slide 19: PDS Nack Code Values (1/9)
Value | Name | Description
0x01 | uet_trimmed | Packet was trimmed. Error Type: NORMAL Source Action: Retransmit (RETX) Reference: Section 3.5.15.1
0x02 | uet_trimmed_lasthop | Packet was trimmed at the last hop switch. Error Type: NORMAL Source Action: Retransmit (RETX) Reference: Section 3.5.15.1
0x03 | uet_trimmed_ack | An ACK carrying read response data was trimmed. Error Type: NORMAL Source Action: Retransmit original read request (RETX) Reference: Section 3.5.15.1

## Slide 20: PDS Nack Code Values (2/9)
Value | Name | Description
0x04 | uet_no_pdc_avail | No PDC resource available; pds.spdcid set to 0. Error Type: NORMAL Source Action: Retransmit (RETRY - no PDC created) Reference: Section 3.5.8.2
0x05 | uet_no_ccc_avail | No CCC resource available; pds.spdcid set to 0. Error Type: NORMAL Source Action: Retransmit (RETRY - no PDC created) Reference: Section 3.5.8.2
0x06 | uet_no_bitmap | No bitmap or other PSN tracking resource available. Error Type: NORMAL Source Action: Retransmit (RETRY - no PDC created) Reference: Section 3.5.8.2

## Slide 21: PDS Nack Code Values (3/9)
Value | Name | Description
0x07 | uet_no_pkt_buffer | No packet buffer resource available. Error Type: NORMAL Source Action: Retransmit (RETX) Reference: Section 3.5.8.2
0x08 | uet_no_gtd_del_avail | No SES guaranteed delivery response resource available. Can't save guaranteed delivery response if needed, packet dropped before SES. Error Type: NORMAL Source Action: Retransmit (RETX) Reference: Section 3.5.8.2
0x09 | uet_no_ses_msg_avail | No message tracking state available. Error Type: NORMAL Source Action: Retransmit (RETX) Reference: Section 3.5.8.2

## Slide 22: PDS Nack Code Values (4/9)
Value | Name | Description
0x0A | uet_no_resource | General resource not available - implementation-specific resource. pds.spdcid set to 0 if no associated PDC. Error Type: NORMAL Source Action: Retransmit (RETX) Reference: Section 3.5.8.2
0x0B | uet_psn_oor_window | PSN outside tracking window (e.g., beyond end of available bitmap). Error Type: NORMAL Source Action: Retransmit (RETX if PSN > CACK) Reference: Section 3.5.8.2
0x0D | uet_rod_ooo | A PSN arrived out of order on a ROD PDC. Error Type: NORMAL Source Action: Retransmit (RETX) Reference: Section 3.5.21.1

## Slide 23: PDS Nack Code Values (5/9)
Value | Name | Description
0x0E | uet_inv_dpdcid | pds.dpdcid is not recognized and pds.flags.syn not set. pds.spdcid set to 0. Error Type: PDC_FATAL Source Action: Close PDC (RETRY) Reference: Section 3.5.8.2
0x0F | uet_pdc_hdr_mismatch | Packet does not have pds.flags.syn set but did not match connection state. Optional check separate from required dpdcid check. pds.spdcid set to 0. Error Type: PDC_FATAL Source Action: Close PDC (RETRY) Reference: Section 3.5.8.2
0x10 | uet_closing | Target PDCID is in closed state or being closed, new PDS Request advances PSN. Error Type: PDC_FATAL (drop packet) Source Action: Report error (RETRY) Reference: Section 3.5.8.3

## Slide 24: PDS Nack Code Values (6/9)
Value | Name | Description
0x11 | uet_closing_in_err | Timeout at target during close process (e.g., no response to Close Request CP). Max_RTO_Retx_Cnt exceeded. Error Type: PDC_FATAL Source Action: Close PDC (no retransmit) Reference: Section 3.5.8.3
0x12 | uet_pkt_not_rcvd | CP arrived with ACK Request but packet with requested PSN was not received. Error Type: PDC_ERR Source Action: Retransmit (RETX) Reference: Section 3.5.16.2
0x13 | uet_gtd_resp_unavail | Duplicate PSN received, state indicates guaranteed delivery SES Response but response cannot be found and PSN was not cleared (implementation error). Error Type: PDC_FATAL Source Action: Close PDC (FAIL, no retransmit) Reference: Section 3.5.16.2

## Slide 25: PDS Nack Code Values (7/9)
Value | Name | Description
0x14 | uet_ack_with_data | ACK Request CP for PSN with associated read response data. Error Type: PDC_ERR Source Action: Retransmit original packet (RETX) Reference: Section 3.5.16.2
0x15 | uet_invalid_syn | Packet received with pds.flags.syn set with pds.psn outside expected range. Error Type: PDC_FATAL Source Action: Close PDC (RETRY) Reference: Section 3.5.8.2
0x16 | uet_pdc_mode_mismatch | Packet received and delivery mode does not match (RUD/ROD). Error Type: PDC_FATAL Source Action: Close PDC (RETRY) Reference: Section 3.5.8.2

## Slide 26: PDS Nack Code Values (8/9)
Value | Name | Description
0x17 | uet_new_start_psn | Resend all packets with new Start_PSN. Error Type: NORMAL Source Action: Retransmit (RETX) Reference: Section 3.5.8.2.1
0x18 | uet_rcvd_ses_procg | SES still processing packet (e.g., delayed packet and retransmission arrive close). Error Type: NORMAL Source Action: Retransmit (ACK may arrive before RETX) Reference: Section 3.5.13
0x19 | uet_unexp_event | Unexpected event - processing requires unsupported feature or implementation error. PDC cannot be recovered. Error Type: PDC_FATAL Source Action: Close PDC (RETRY) Reference: Generic event, implementation specific

## Slide 27: PDS Nack Code Values (9/9)
Value | Name | Description
0x1A | uet_rcvr_infer_loss | Destination infers a PSN was lost and effectively requests retransmission. Application specific. Error Type: NORMAL Source Action: Retransmit (RETX) Reference: Section 3.5.15
0xFD | uet_exp_nack_normal | Experimental NACK code - NORMAL error type. Error Type: NORMAL Source Action: Retransmit (RETX)
0xFE | uet_exp_nack_err | Experimental NACK code - PDC_ERR error type. Error Type: PDC_ERR Source Action: Retransmit (RETRY)
0xFF | uet_exp_nack_fatal | Experimental NACK code - PDC_FATAL error type. Error Type: PDC_FATAL Source Action: Close PDC (FAIL)

## Slide 28: PDS Nack Error Type Values
Value | Name | Description
0x00 | normal | Normal operation, retransmit expected
0x01 | pdc_err | PDC error, retransmit may help
0x02 | pdc_fatal | Fatal PDC error, PDC should be closed

## Slide 29: PDS Nack Source Action Values
Value | Name | Description
0x00 | retx | Retransmit the packet
0x01 | retry | Retry with new PDC establishment
0x02 | fail | Report failure, do not retry

## Slide 30: SES Request Opcode Values
Value | Name | Description
0x00 | tagged_send | 
0x01 | rma_write | 
0x02 | rma_read | 
0x03 | atomic_write | 
0x04 | atomic_read | 
0x05 | atomic_compare_swap | 
0x06 | deferrable_send | 
0x07 | ready_to_restart | 
0x08 | small_message | 
0x09 | small_rma_write | 
0x0A | small_rma_read | 
0x0B | small_atomic_write | 
0x0C | small_atomic_read | 
0x0D | small_atomic_compare_swap | 
0x0E | reserved_0e | 
0x0F | reserved_0f | 

## Slide 31: SES Response Opcode Values
Value | Name | Description
0x00 | response | 
0x01 | response_with_data | 
0x02 | optimized_response_with_data | 
0x03 | nack | 
0x04 | reserved_04 | 
0x05 | reserved_05 | 
0x06 | reserved_06 | 
0x07 | reserved_07 | 

## Slide 32: CMS Cc Type Values (1/4)
Value | Name | Description
0x00 | cc_nscc | CC_NSCC - Network-Signaled Congestion Control. When cc_type = 0, the pds.ack_cc_state field uses the NSCC format defined in Table 3-74 (8 bytes): - service_time (16 bits) - restore cwnd / rc (1 bit) - rcv_cwnd_pend (7 bits) - rcvd_bytes (24 bits) - ooo_count (16 bits) NSCC uses network-signaled congestion control where the destination communicates congestion state back to the source via ACK packets. UE Spec: Table 3-48, mnemonic "CC_NSCC"

## Slide 33: CMS Cc Type Values (2/4)
Value | Name | Description
0x01 | cc_credit | CC_CREDIT - Credit-based flow control (TFC, RCCC). When cc_type = 1, the pds.ack_cc_state field uses the credit format defined in Table 3-75 (8 bytes total, 64 bits): - credit (24 bits) - reserved (24 bits, must be 0) - ooo_count (16 bits) Note: Table 3-75 defines only credit(24)+ooo_count(16)=40 bits, but pds.ack_cc_state in ACK_CC is always 64 bits, so 24 bits of reserved padding are added between credit and ooo_count. Used with TFC (Traffic Flow Control) and RCCC (Rate-Based Congestion Control) when NSCC is not enabled. UE Spec: Table 3-48, mnemonic "CC_CREDIT"
0x02 | reserved_2 | Reserved for future use

## Slide 34: CMS Cc Type Values (3/4)
Value | Name | Description
0x03 | reserved_3 | Reserved for future use
0x04 | reserved_4 | Reserved for future use
0x05 | reserved_5 | Reserved for future use
0x06 | reserved_6 | Reserved for future use
0x07 | reserved_7 | Reserved for future use
0x08 | reserved_8 | Reserved for future use
0x09 | reserved_9 | Reserved for future use
0x0A | reserved_10 | Reserved for future use
0x0B | reserved_11 | Reserved for future use
0x0C | reserved_12 | Reserved for future use
0x0D | reserved_13 | Reserved for future use
0x0E | proprietary_14 | Reserved for proprietary extensions. Values 14-15 are reserved for vendor-specific congestion control algorithms. The format of pds.ack_cc_state when using these values is implementation-defined.

## Slide 35: CMS Cc Type Values (4/4)
Value | Name | Description
0x0F | proprietary_15 | Reserved for proprietary extensions. Values 14-15 are reserved for vendor-specific congestion control algorithms. The format of pds.ack_cc_state when using these values is implementation-defined.

## Slide 36: CBFC Cbfc Message Type Values
Value | Name | Description
0x10 | cf_update | CF_Update CtlOS message (credit freed updates for 2 VCs)

## Slide 37: UE Protocol State Machines
State machine definitions extracted from KSY datamodel files

## Slide 38: CCC State Machine States (1/2)
State | Description
IDLE | CCC has no pending data. All data has been ACKed. CCC can be removed when in this state. UE Spec: Figure 3-98, IDLE state UE Spec: Lines 9162 (IDLE definition)
ACTIVE | CCC has data to send but congestion control does not permit sending. Waiting for window space (NSCC) or credit (RCCC/TFC). UE Spec: Figure 3-98, ACTIVE state UE Spec: Lines 9156-9157 (ACTIVE definition)
READY | CCC has data to send and congestion control permits sending. Scheduler can select PDCs associated with this CCC. UE Spec: Figure 3-98, READY state UE Spec: Lines 9157-9160 (READY definition)

## Slide 39: CCC State Machine States (2/2)
State | Description
PENDING | CCC has sent all pending data but waiting for ACKs. No new data to send, but data is in flight. UE Spec: Figure 3-98, PENDING state UE Spec: Lines 9161-9164 (PENDING definition)

## Slide 40: CCC State Machine Transitions (1/2)
From | To | Trigger | Condition | Action
IDLE | ACTIVE | new data arrives | New data posted to any PDC associated with CCC | CCC becomes active Check if congestion control permits sending
ACTIVE | READY | congestion control permits sending | (NSCC: cwnd has space) ¦¦ (RCCC/TFC: credit available) | CCC ready for scheduling PDCs can be selected for transmission
ACTIVE | PENDING | no data to send, last retransmit ACKed | No new data && no packets marked for retransmission && last retransmit ACKed | All pending work sent Wait for ACKs
READY | READY | data sent but more to send | Data transmitted && more data pending && CC permits | Continue in READY state Scheduler can select more PDCs
READY | ACTIVE | congestion control no longer permits sending | (NSCC: cwnd exhausted) ¦¦ (RCCC/TFC: credit exhausted) | Wait for ACKs to free window/credit

## Slide 41: CCC State Machine Transitions (2/2)
From | To | Trigger | Condition | Action
READY | PENDING | all data sent | No more new data && no packets marked for retransmission | All pending work sent Wait for ACKs
PENDING | IDLE | all data ACKed | All data on all PDCs associated with CCC has been ACKed | CCC can be removed No pending work
PENDING | ACTIVE | retransmission needed | NACK received ¦¦ loss inferred from SACK ¦¦ RTO expired | Mark packet for retransmission Check if CC permits sending

## Slide 42: VC State Machine States
State | Description
DISABLED | DISABLED state
INITIALIZING | INITIALIZING state
ACTIVE | ACTIVE state
REMOVING | REMOVING state (terminal)

## Slide 43: VC State Machine Transitions
From | To | Trigger | Condition | Action
DISABLED | INITIALIZING | start | true | Begin processing

## Slide 44: LLR Transmit State Machine States (1/2)
State | Description
LLR_OFF | LLR is disabled. TX LLR uses BEST_EFFORT style for LLR-desired frames. No LLR processing occurs. UE Spec: Figure 5-3, LLR_OFF state
INIT | LLR initialization state. Sends LLR_INIT CtlOS periodically. Waits for LLR_INIT_ECHO from link partner. UE Spec: Figure 5-3, INIT state UE Spec: Section 5.1.9.1.1 (LLR_INIT CtlOS)
ADVANCE | Normal operation state. Accepts new LLR-desired frames. Transmits frames and manages replay buffer. UE Spec: Figure 5-3, ADVANCE state

## Slide 45: LLR Transmit State Machine States (2/2)
State | Description
REPLAY | Replay state. Retransmits frames from replay buffer. Entered on NACK reception or replay_timer expiry. UE Spec: Figure 5-3, REPLAY state UE Spec: Lines 12296 (NACK triggers REPLAY)
FLUSH | Flush state. Discards all frames in replay buffer. Entered when replay_ct reaches replay_ct_max. UE Spec: Figure 5-3, FLUSH state UE Spec: Lines 12298-12300 (FLUSH behavior)

## Slide 46: LLR Transmit State Machine Transitions (1/3)
From | To | Trigger | Condition | Action
LLR_OFF | INIT | llr_mode_local set to ON | llr_mode_local == ON | Initialize tx_seq Set last_ack_seq = init_seq - 1 Start sending LLR_INIT CtlOS
INIT | ADVANCE | init_echo_received pulse | LLR_INIT_ECHO received with init_seq == tx_seq | LLR initialization complete Begin normal frame transmission Start replay_timer
INIT | LLR_OFF | llr_mode_local set to OFF | llr_mode_local == OFF | Disable LLR Clear replay buffer

## Slide 47: LLR Transmit State Machine Transitions (2/3)
From | To | Trigger | Condition | Action
ADVANCE | REPLAY | nack_received or replay_timer expiry | (nack_received == TRUE) ¦¦ (replay_timer expired && replay_ct < replay_ct_max) | Complete current frame transmission Set nack_received = FALSE Set replay_ct = 0 Begin replay from replay buffer
ADVANCE | FLUSH | replay_timer expiry with max retries | replay_timer expired && replay_ct == replay_ct_max && replay_ct_max != 255 | Enter FLUSH state Prepare to discard replay buffer
ADVANCE | FLUSH | pcs_lost_status_timer expiry | pcs_lost_status_timer expired | Link lost, enter FLUSH state
ADVANCE | LLR_OFF | llr_mode_local set to OFF | llr_mode_local == OFF | Disable LLR Clear replay buffer

## Slide 48: LLR Transmit State Machine Transitions (3/3)
From | To | Trigger | Condition | Action
REPLAY | ADVANCE | replay complete | All frames in replay buffer retransmitted | Increment replay_ct Resume normal operation Restart replay_timer
REPLAY | FLUSH | pcs_lost_status_timer expiry | pcs_lost_status_timer expired | Link lost during replay
REPLAY | LLR_OFF | llr_mode_local set to OFF | llr_mode_local == OFF | Disable LLR Clear replay buffer
FLUSH | INIT | re_init_on_discard | re_init_on_discard == TRUE | Reinitialize LLR Start sending LLR_INIT CtlOS
FLUSH | LLR_OFF | llr_mode_local set to OFF or !re_init_on_discard | llr_mode_local == OFF ¦¦ re_init_on_discard == FALSE | Disable LLR or stay off

## Slide 49: PDS Header Building Blocks
Packet Delivery Sublayer Format Definitions

## Slide 50: PDS Wire Formats (14 files)
Type | Format | KSY File | Size | Description
0x01 | RUD Request | rud_rod_request.ksy | 12B | Reliable Unordered Delivery
0x02 | ROD Request | rud_rod_request.ksy | 12B | Reliable Ordered Delivery
0x04 | RUDI Request | rudi_request_response.ksy | 6B | Reliable Unordered Immediate
0x05 | RUDI Response | rudi_request_response.ksy | 6B | RUDI response
0x06 | UUD Request | uud_request.ksy | 6B | Unreliable Unordered Delivery
0x07 | ACK | rud_rod_ack.ksy | 12B | Acknowledgment
0x08 | ACK_CC | ack_cc.ksy | 28B | ACK with CC state
0x09 | ACK_CCX | ack_ccx.ksy | 44B | ACK with extended CC
0x0A | NACK | nack.ksy | 12B | Negative acknowledgment
0x0B | CP | rud_rod_cp.ksy | 12B | Control packet (10 subtypes)
0x0C | NACK_CCX | nack_ccx.ksy | 28B | NACK with extended CC
0x0D | RUD_CC_REQ | rud_rod_request_cc.ksy | 28B | RUD with CC state
0x0E | ROD_CC_REQ | rud_rod_request_cc.ksy | 28B | ROD with CC state
- | Prologue | prologue.ksy | 2B | PDS header prologue
- | Entropy Header | entropy_header.ksy | 4B | ECMP entropy (non-UDP)
- | Default SES | rud_rod_default_ses.ksy | 8B | Default SES response
- | NACK Codes | nack_codes.ksy | - | NACK reason codes enum

## Slide 51: PDS Protocol State Machines (16 files)
Protocol | KSY File | UE Spec Section | Description
PDC Establishment | pdc_establishment.ksy | 3.5.7 | PDC setup handshake
PDC Close | pdc_close.ksy | 3.5.7 | PDC teardown
PDC Initiator | pdc_initiator.ksy | 3.5.7 | Initiator state machine
PDC Target | pdc_target.ksy | 3.5.7 | Target state machine
PDS Manager | pds_manager.ksy | 3.5.7 | PDS management
RUD Delivery | rud_delivery.ksy | 3.5.10.3 | RUD delivery protocol
ROD Delivery | rod_delivery.ksy | 3.5.10.3 | ROD delivery protocol
RUDI Delivery | rudi_delivery.ksy | 3.5.10.9 | RUDI delivery protocol
Loss Detection CACK/SACK | loss_detection_cack_sack.ksy | 3.5.11 | Cumulative/Selective ACK
Loss Detection EV | loss_detection_ev.ksy | 3.5.11 | Early validation
Loss Detection NACK | loss_detection_nack.ksy | 3.5.11 | NACK-based detection
Loss Detection OOO | loss_detection_ooo.ksy | 3.5.11 | Out-of-order detection
Loss Detection Receiver | loss_detection_receiver.ksy | 3.5.11 | Receiver-side detection
Loss Detection RTO | loss_detection_rto.ksy | 3.5.11 | Retransmit timeout
Loss Detection Tail | loss_detection_tail.ksy | 3.5.11 | Tail loss detection
Loss Detection Trimming | loss_detection_trimming.ksy | 3.5.11 | Trimmed packet detection

## Slide 52: SES Header Building Blocks
Semantic Sublayer Format Definitions

## Slide 53: SES Wire Formats (15 files)
next_hdr | Format | KSY File | Size | Description
0x0 | Standard Request SOM=1 | standard_request_som1.ksy | 44B | Start of message
0x1 | Standard Request SOM=0 | standard_request_som0.ksy | 16B | Continuation
0x2 | Optimized Non-Matching | optimized_non_matching.ksy | 32B | Optimized RMA
0x3 | Small Message | small_message.ksy | 32B | Single-packet optimized
0x3 | Small RMA | small_rma.ksy | 32B | Small RMA operations
0x4 | Response | response.ksy | 16B | Standard response
0x5 | Response with Data | response_with_data.ksy | 24B | Data-carrying response
0x6 | Optimized Response | optimized_response_with_data.ksy | 16B | Optimized format
- | Rendezvous Extension | rendezvous_extension.ksy | 32B | Large message protocol
- | Atomic Extension | atomic_extension.ksy | 8B | Atomic operations
- | CAS Extension | cas_extension.ksy | 40B | Compare-and-swap
- | Deferrable Send | deferrable_send_request.ksy | 44B | Deferrable send request
- | Ready to Restart | ready_to_restart.ksy | 44B | RTR response
- | Opcodes | opcodes.ksy | - | SES opcode definitions
- | Next Header Types | next_header_types.ksy | - | Header type enum

## Slide 54: SES Message Sequences (12 files)
Sequence | KSY File | Description
Single Packet Request | single_packet_request.ksy | Single-packet message flow
Multi Packet Request | multi_packet_request.ksy | Multi-packet message flow
Read Standard | read_standard.ksy | Standard RDMA read
Read Large ACK | read_large_ack.ksy | Large read with ACK
Rendezvous Expected | rendezvous_expected.ksy | Rendezvous with posted receive
Rendezvous Unexpected | rendezvous_unexpected.ksy | Rendezvous without posted receive
Deferrable Expected | deferrable_expected.ksy | Deferrable with buffer
Deferrable Unexpected | deferrable_unexpected.ksy | Deferrable without buffer
Deferrable No Buffer | deferrable_no_buffer.ksy | Deferrable RTR flow
Buffered Messages | buffered_messages.ksy | Message buffering
Buffered Headers | buffered_headers.ksy | Header buffering
Backoff Retry | backoff_retry.ksy | Retry with backoff

## Slide 55: CMS Header Building Blocks
Congestion Management Sublayer Format Definitions

## Slide 56: CMS Wire Formats (7 files)
Format | KSY File | Size | Description
ACK CC State NSCC | ack_cc_state_nscc.ksy | 8B | NSCC congestion state
ACK CC State RCCC/TFC | ack_cc_state_rccc_tfc.ksy | 8B | Credit-based CC state
Request CC State | req_cc_state.ksy | 8B | Source CC state
Credit CP Payload | credit_cp_payload.ksy | Var | Credit control packet
Credit Request Payload | credit_request_cp_payload.ksy | Var | Credit request
CC Type | cc_type.ksy | - | CC algorithm type enum
CCX Type | ccx_type.ksy | - | Extended CC type enum

## Slide 57: CMS Protocol State Machines (8 files)
Protocol | KSY File | UE Spec Section | Description
CCC State Machine | ccc_state_machine.ksy | 3.6.6 | Congestion Control Context
NSCC Source | nscc_source.ksy | 3.6.13.3-6 | NSCC source algorithm
NSCC Destination | nscc_destination.ksy | 3.6.13.9 | NSCC destination algorithm
RCCC Source | rccc_source.ksy | 3.6.14.2-4 | RCCC source algorithm
RCCC Destination | rccc_destination.ksy | 3.6.14.6 | RCCC destination algorithm
TFC Source | tfc_source.ksy | 3.6.15 | TFC source algorithm
TFC Destination | tfc_destination.ksy | 3.6.15 | TFC destination algorithm
Multipath Selection | multipath_selection.ksy | 3.6.16 | ECMP path selection

## Slide 58: TSS Header Building Blocks
Transport Security Sublayer Format Definitions

## Slide 59: TSS Wire Formats (2 files)
Format | KSY File | Size | Description
Security Header | security_header.ksy | 12-16B | AES-GCM encryption header
IV Construction | iv_construction.ksy | 12B | Initialization vector

## Slide 60: TSS Protocol State Machines (7 files)
Protocol | KSY File | UE Spec Section | Description
TSS TX Processing | tss_tx_processing.ksy | 3.7 | Transmit encryption
TSS RX Processing | tss_rx_processing.ksy | 3.7 | Receive decryption
Key Rotation | key_rotation.ksy | 3.7 | Key rotation protocol
Join Secure Domain | join_secure_domain.ksy | 3.7 | Domain join protocol
KDF Direct | kdf_direct.ksy | 3.7 | Direct key derivation
KDF Client Server | kdf_client_server.ksy | 3.7 | Client-server KDF
KDF Cluster | kdf_cluster.ksy | 3.7 | Cluster KDF

## Slide 61: Link Layer Building Blocks
LLR, CBFC, and LLDP Format Definitions

## Slide 62: LLR Wire Formats (6 files)
Type | Format | KSY File | Size | Description
0x01 | LLR_ACK | llr_ack_ctlos.ksy | 8B | Frame acknowledgment
0x02 | LLR_NACK | llr_nack_ctlos.ksy | 8B | Negative acknowledgment
0x03 | LLR_INIT | llr_init_ctlos.ksy | 8B | Initialize sequence state
0x04 | LLR_INIT_ECHO | llr_init_echo_ctlos.ksy | 8B | Confirm initialization
- | Preamble MII | llr_preamble_mii.ksy | 8B | MII preamble format
- | Preamble 64B/66B | llr_preamble_64b66b.ksy | 8B | 64B/66B preamble format

## Slide 63: LLR Protocol State Machines (3 files)
Protocol | KSY File | UE Spec Section | Description
LLR Transmit | llr_transmit_sm.ksy | 5.1 | Transmit state machine
LLR Receive | llr_receive.ksy | 5.1 | Receive state machine
ACK/NACK Transmit | ack_nack_transmit_sm.ksy | 5.1 | ACK/NACK generation

## Slide 64: CBFC Wire Formats (2 files)
Format | KSY File | Size | Description
CF_Update | cf_update.ksy | 8B | Credit freed (CtlOS)
CC_Update | cc_update.ksy | 8B | Credit consumed (Ethernet)

## Slide 65: CBFC Protocol State Machines (3 files)
Protocol | KSY File | UE Spec Section | Description
VC State Machine | vc_state_machine.ksy | 5.2 | Virtual channel state
Lossless VC Init | lossless_vc_init.ksy | 5.2 | Lossless VC initialization
Lossless VC Removal | lossless_vc_removal.ksy | 5.2 | Lossless VC removal

## Slide 66: LLDP TLV Formats (3 files)
Format | KSY File | Description
Link Negotiation TLV | ue_link_negotiation_tlv.ksy | LLR/CBFC enable flags
CBFC TLV | ue_cbfc_tlv.ksy | VC configuration
Link Negotiation SM | link_negotiation_sm.ksy | Negotiation state machine

## Slide 67: Network and Physical Layer
Network Formats and Physical Layer Definitions

## Slide 68: Network Layer Formats (4 files)
Format | KSY File | Description
DSCP Categories | dscp_categories.ksy | DSCP category mappings
Packet Trimming | packet_trimming.ksy | Trimming mechanism
UFH 16-bit | ufh_16.ksy | 16-bit UE Fabric Header
UFH 32-bit | ufh_32.ksy | 32-bit UE Fabric Header

## Slide 69: Physical Layer Formats (1 file)
Format | KSY File | Description
Control Ordered Sets | control_ordered_sets.ksy | 64B/66B CtlOS encoding

## Slide 70: PDS Packet Variant Matrix
Delivery Modes and Response Types

## Slide 71: PDS Delivery Modes
Mode | Type | Reliability | Ordering | Use Case
RUD | 0x01 | Reliable | Unordered | General RDMA
ROD | 0x02 | Reliable | Ordered | Streaming, multi-packet
RUDI | 0x04/0x05 | Reliable | Unordered | Idempotent operations
UUD | 0x06 | Unreliable | Unordered | Best-effort traffic

## Slide 72: PDS Request/Response Mapping
Request Type | Possible Responses | KSY Files
RUD Request (0x01) | ACK, ACK_CC, ACK_CCX, NACK, NACK_CCX | rud_rod_request.ksy, rud_rod_ack.ksy, ack_cc.ksy, ack_ccx.ksy, nack.ksy, nack_ccx.ksy
ROD Request (0x02) | ACK, ACK_CC, ACK_CCX, NACK, NACK_CCX | rud_rod_request.ksy, rud_rod_ack.ksy, ack_cc.ksy, ack_ccx.ksy, nack.ksy, nack_ccx.ksy
RUDI Request (0x04) | RUDI Response, NACK | rudi_request_response.ksy, nack.ksy
UUD Request (0x06) | (no response) | uud_request.ksy
Control Packet (0x0B) | (varies by subtype) | rud_rod_cp.ksy

## Slide 73: Control Packet Subtypes
ctl_type | Name | Direction | Description
0 | NOOP | Either | No operation
1 | ACK_REQUEST | Src->Dst | Request ACK for specific PSN
2 | CLEAR_COMMAND | Init->Tgt | Clear guaranteed delivery state
3 | CLEAR_REQUEST | Tgt->Init | Request initiator to send clear
4 | CLOSE_COMMAND | Init->Tgt | PDC is being closed
5 | CLOSE_REQUEST | Tgt->Init | Request initiator to close PDC
6 | PROBE | Src->Dst | Request PDS ACK
7 | CREDIT | Dst->Src | Carry CC credit
8 | CREDIT_REQUEST | Src->Dst | Request credit
9 | NEGOTIATION | Either | PDC negotiation

## Slide 74: SES Packet Variant Matrix
Operation Types and Header Formats

## Slide 75: SES Request Opcodes
Opcode | Value | KSY File | Description
Tagged Send | 0x00 | standard_request_som1.ksy | Send with tag matching
RMA Write | 0x01 | standard_request_som1.ksy | Remote memory write
RMA Read | 0x02 | standard_request_som1.ksy | Remote memory read
Atomic Write | 0x03 | atomic_extension.ksy | Atomic memory write
Atomic Read | 0x04 | atomic_extension.ksy | Atomic memory read
Atomic CAS | 0x05 | cas_extension.ksy | Compare-and-swap
Deferrable Send | 0x06 | deferrable_send_request.ksy | Deferrable send
Ready to Restart | 0x07 | ready_to_restart.ksy | Restart notification
Small Message | 0x08 | small_message.ksy | Small message (32B header)
Small RMA Write | 0x09 | small_rma.ksy | Small RMA write
Small RMA Read | 0x0A | small_rma.ksy | Small RMA read
Small Atomic Write | 0x0B | atomic_extension.ksy | Small atomic write
Small Atomic Read | 0x0C | atomic_extension.ksy | Small atomic read
Small Atomic CAS | 0x0D | cas_extension.ksy | Small atomic CAS

## Slide 76: SES Response Opcodes
Opcode | Value | KSY File | Description
Response | 0x00 | response.ksy | Standard response
Response with Data | 0x01 | response_with_data.ksy | Response carrying data
Optimized Response | 0x02 | optimized_response_with_data.ksy | Optimized format
NACK | 0x03 | response.ksy | Negative acknowledgment

## Slide 77: Detailed Packet Structures
Wire Format Diagrams

## Slide 78: PDS Prologue (2 bytes) - prologue.ksy (text)
+-------+-------+-------+-------+-------+-------+-------+-------+
| Byte 0 | Byte 1 |
+-------+-------+-------+-------+-------+-------+-------+-------+
| type[4:0] | next_hdr/ctl[3:0] | flags[6:0] |
+-------+-------+-------+-------+-------+-------+-------+-------+

## Slide 79: RUD/ROD Request (12 bytes) - rud_rod_request.ksy (text)
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
|type |nxt|flg| clear_psn_offset | PSN [31:0] ->
+-------+-------+-------+-------+-------+-------+-------+-------+
8 9 10 11
+-------+-------+-------+-------+
-> | spdcid | dpdcid |
+-------+-------+-------+-------+

## Slide 80: ACK_CC (28 bytes) - ack_cc.ksy (text)
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
| ACK Header (12 bytes) |
+-------+-------+-------+-------+-------+-------+-------+-------+
8 9 10 11 12 13 14 15
+-------+-------+-------+-------+-------+-------+-------+-------+
| (ACK cont'd) |cc_typ|cc_flg| mpr | sack_psn_offset ->
+-------+-------+-------+-------+-------+-------+-------+-------+
16 17 18 19 20 21 22 23
+-------+-------+-------+-------+-------+-------+-------+-------+
-> | sack_bitmap [63:0] |
+-------+-------+-------+-------+-------+-------+-------+-------+
24 25 26 27
+-------+-------+-------+-------+
| ack_cc_state [63:0] |
+-------+-------+-------+-------+

## Slide 81: SES Standard Request SOM=1 (44 bytes) - standard_request_som1.ksy (text)
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
|rs|opcode |v|dc|ie|rl|hd|eo|so| message_id | ri_gen ->
+-------+-------+-------+-------+-------+-------+-------+-------+
8 9 10 11 12 13 14 15
+-------+-------+-------+-------+-------+-------+-------+-------+
-> | job_id [23:0] |rsvd|pid_on_fep |rsvd| resource_idx ->
+-------+-------+-------+-------+-------+-------+-------+-------+
16 17 18 19 20 21 22 23
+-------+-------+-------+-------+-------+-------+-------+-------+
-> | buffer_offset [63:0] |
+-------+-------+-------+-------+-------+-------+-------+-------+
24 25 26 27 28 29 30 31
+-------+-------+-------+-------+-------+-------+-------+-------+
| initiator [31:0] | match_bits / memory_key ->
+-------+-------+-------+-------+-------+-------+-------+-------+
32 33 34 35 36 37 38 39
+-------+-------+-------+-------+-------+-------+-------+-------+
-> | (match_bits cont'd) [63:0] | header_data [63:0] ->
+-------+-------+-------+-------+-------+-------+-------+-------+
40 41 42 43
+-------+-------+-------+-------+
-> | (hdr_data) | request_length|
+-------+-------+-------+-------+

## Slide 82: TSS Security Header (16 bytes, sp=1) - security_header.ksy (text)
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
|type|sp|r|an| sdi [23:0] | ssi [31:0] |
+-------+-------+-------+-------+-------+-------+-------+-------+
8 9 10 11 12 13 14 15
+-------+-------+-------+-------+-------+-------+-------+-------+
| tsc [63:0] |
| epoch [15:0] | counter [47:0] |
+-------+-------+-------+-------+-------+-------+-------+-------+

## Slide 83: LLR_ACK CtlOS (8 bytes) - llr_ack_ctlos.ksy (text)
64B/66B Block (Sync Header = 2'b10):
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
| 0x4B | 0x01 |ack_nack_seq |seq_lo | Rsvd | Rsvd | Rsvd |
| (BTF) | (ACK) | [19:12]|[11:4]|+O-code| | | |
+-------+-------+-------+-------+-------+-------+-------+-------+
D0 D1 D2 D3 D4 D5 D6 D7

## Slide 84: CF_Update CtlOS (8 bytes) - cf_update.ksy (text)
64B/66B Block (Sync Header = 2'b10):
Byte: 0 1 2 3 4 5 6 7
+-------+-------+-------+-------+-------+-------+-------+-------+
| 0x5C | 0x10 |CF1_VC |CF1_cnt|CF1_cnt|CF2_VC |CF2_cnt|CF2_cnt|
| (Ctrl)| (Type)|+cnt_hi| [10:3]|lo+Ocd |+cnt_hi| [10:3]|lo+Rsvd|
+-------+-------+-------+-------+-------+-------+-------+-------+
D0 D1 D2 D3 D4 D5 D6 D7

## Slide 85: State Machines Summary
38 Protocol State Machines Across All Sublayers

## Slide 86: Transport Layer State Machines (31 files) (1/2)
Sublayer | State Machine | KSY File | States
PDS | PDC Establishment | pdc_establishment.ksy | IDLE, SYN_SENT, SYN_RCVD, ESTABLISHED
PDS | PDC Close | pdc_close.ksy | ESTABLISHED, CLOSE_WAIT, LAST_ACK, CLOSED
PDS | PDC Initiator | pdc_initiator.ksy | IDLE, CONNECTING, CONNECTED, CLOSING
PDS | PDC Target | pdc_target.ksy | IDLE, LISTENING, CONNECTED, CLOSING
PDS | PDS Manager | pds_manager.ksy | INIT, ACTIVE, SHUTDOWN
PDS | RUD Delivery | rud_delivery.ksy | IDLE, SENDING, WAITING_ACK, COMPLETE
PDS | ROD Delivery | rod_delivery.ksy | IDLE, SENDING, WAITING_ACK, COMPLETE
PDS | RUDI Delivery | rudi_delivery.ksy | IDLE, SENDING, WAITING_RESPONSE
PDS | Loss Detection CACK/SACK | loss_detection_cack_sack.ksy | MONITOR, DETECT, RETRANSMIT
PDS | Loss Detection EV | loss_detection_ev.ksy | MONITOR, VALIDATE, SIGNAL
PDS | Loss Detection NACK | loss_detection_nack.ksy | MONITOR, NACK_RCVD, RETRANSMIT
PDS | Loss Detection OOO | loss_detection_ooo.ksy | MONITOR, OOO_DETECT, SIGNAL
PDS | Loss Detection Receiver | loss_detection_receiver.ksy | MONITOR, GAP_DETECT, NACK_SEND
PDS | Loss Detection RTO | loss_detection_rto.ksy | IDLE, TIMER_RUNNING, TIMEOUT
PDS | Loss Detection Tail | loss_detection_tail.ksy | MONITOR, TAIL_DETECT, PROBE
PDS | Loss Detection Trimming | loss_detection_trimming.ksy | MONITOR, TRIM_DETECT, RETRANSMIT
CMS | CCC State Machine | ccc_state_machine.ksy | IDLE, ACTIVE, READY, PENDING
CMS | NSCC Source | nscc_source.ksy | IDLE, SLOW_START, CONG_AVOID, FAST_RECOVERY

## Slide 87: Transport Layer State Machines (31 files) (2/2)
Sublayer | State Machine | KSY File | States
CMS | NSCC Destination | nscc_destination.ksy | IDLE, MONITOR, SIGNAL_CONGESTION
CMS | RCCC Source | rccc_source.ksy | IDLE, RATE_CONTROL, BACKOFF
CMS | RCCC Destination | rccc_destination.ksy | IDLE, MONITOR_BUFFER, REQUEST_REDUCTION
CMS | TFC Source | tfc_source.ksy | IDLE, FLOW_CONTROL, THROTTLE
CMS | TFC Destination | tfc_destination.ksy | IDLE, MONITOR, SIGNAL_THROTTLE
CMS | Multipath Selection | multipath_selection.ksy | IDLE, SELECT_PATH, MONITOR_PATHS
TSS | TSS TX Processing | tss_tx_processing.ksy | IDLE, ENCRYPT, SEND
TSS | TSS RX Processing | tss_rx_processing.ksy | IDLE, DECRYPT, VALIDATE
TSS | Key Rotation | key_rotation.ksy | ACTIVE, ROTATING, COMPLETE
TSS | Join Secure Domain | join_secure_domain.ksy | INIT, JOINING, JOINED
TSS | KDF Direct | kdf_direct.ksy | INIT, DERIVE, COMPLETE
TSS | KDF Client Server | kdf_client_server.ksy | INIT, REQUEST, RECEIVE, COMPLETE
TSS | KDF Cluster | kdf_cluster.ksy | INIT, DISTRIBUTE, COMPLETE

## Slide 88: Link Layer State Machines (7 files)
Sublayer | State Machine | KSY File | States
LLR | LLR Transmit | llr_transmit_sm.ksy | IDLE, TRANSMIT, WAIT_ACK, RETRANSMIT
LLR | LLR Receive | llr_receive.ksy | IDLE, RECEIVE, VALIDATE, DELIVER
LLR | ACK/NACK Transmit | ack_nack_transmit_sm.ksy | IDLE, GENERATE, SEND
CBFC | VC State Machine | vc_state_machine.ksy | INIT, ACTIVE, PAUSED, SHUTDOWN
CBFC | Lossless VC Init | lossless_vc_init.ksy | INIT, NEGOTIATE, ACTIVE
CBFC | Lossless VC Removal | lossless_vc_removal.ksy | ACTIVE, DRAINING, REMOVED
LLDP | Link Negotiation | link_negotiation_sm.ksy | INIT, NEGOTIATE, COMPLETE

## Slide 89: Header Overhead Summary
Packet Size Analysis

## Slide 90: Minimum Header Sizes by Delivery Mode
Delivery Mode | PDS Header | SES Header | Total Overhead | KSY Files
RUD (standard) | 12B | 44B (SOM=1) | 56B | rud_rod_request.ksy, standard_request_som1.ksy
RUD (continuation) | 12B | 16B (SOM=0) | 28B | rud_rod_request.ksy, standard_request_som0.ksy
RUD (small msg) | 12B | 32B | 44B | rud_rod_request.ksy, small_message.ksy
RUD with CC | 28B | 44B (SOM=1) | 72B | rud_rod_request_cc.ksy, standard_request_som1.ksy
RUDI | 6B | 44B (SOM=1) | 50B | rudi_request_response.ksy, standard_request_som1.ksy
UUD | 6B | 44B (SOM=1) | 50B | uud_request.ksy, standard_request_som1.ksy

## Slide 91: Response Header Sizes
Response Type | PDS Header | SES Header | Total | KSY Files
ACK | 12B | - | 12B | rud_rod_ack.ksy
ACK_CC | 28B | - | 28B | ack_cc.ksy
ACK_CCX | 44B | - | 44B | ack_ccx.ksy
NACK | 12B | - | 12B | nack.ksy
NACK_CCX | 28B | - | 28B | nack_ccx.ksy
SES Response | 12B | 16B | 28B | rud_rod_ack.ksy, response.ksy
SES Response w/Data | 12B | 24B | 36B | rud_rod_ack.ksy, response_with_data.ksy
RUDI Response | 6B | 16B | 22B | rudi_request_response.ksy, response.ksy

## Slide 92: Complete Datamodel Coverage
All 103 UE KSY Files

## Slide 93: transport/pds/ (30 files) (1/2)
Category | File | Description
Format | prologue.ksy | PDS header prologue (2B)
Format | rud_rod_request.ksy | RUD/ROD request (12B)
Format | rud_rod_request_cc.ksy | RUD/ROD request with CC (28B)
Format | rudi_request_response.ksy | RUDI request/response (6B)
Format | uud_request.ksy | UUD request (6B)
Format | rud_rod_ack.ksy | ACK (12B)
Format | ack_cc.ksy | ACK_CC (28B)
Format | ack_ccx.ksy | ACK_CCX (44B)
Format | nack.ksy | NACK (12B)
Format | nack_ccx.ksy | NACK_CCX (28B)
Format | nack_codes.ksy | NACK reason codes
Format | rud_rod_cp.ksy | Control packet (12B)
Format | entropy_header.ksy | Entropy header (4B)
Format | rud_rod_default_ses.ksy | Default SES response (8B)
Protocol | pdc_establishment.ksy | PDC establishment SM
Protocol | pdc_close.ksy | PDC close SM
Protocol | pdc_initiator.ksy | PDC initiator SM
Protocol | pdc_target.ksy | PDC target SM

## Slide 94: transport/pds/ (30 files) (2/2)
Category | File | Description
Protocol | pds_manager.ksy | PDS manager SM
Protocol | rud_delivery.ksy | RUD delivery SM
Protocol | rod_delivery.ksy | ROD delivery SM
Protocol | rudi_delivery.ksy | RUDI delivery SM
Protocol | loss_detection_cack_sack.ksy | CACK/SACK loss detection
Protocol | loss_detection_ev.ksy | Early validation loss detection
Protocol | loss_detection_nack.ksy | NACK loss detection
Protocol | loss_detection_ooo.ksy | OOO loss detection
Protocol | loss_detection_receiver.ksy | Receiver loss detection
Protocol | loss_detection_rto.ksy | RTO loss detection
Protocol | loss_detection_tail.ksy | Tail loss detection
Protocol | loss_detection_trimming.ksy | Trimming loss detection

## Slide 95: transport/ses/ (27 files) (1/2)
Category | File | Description
Format | standard_request_som1.ksy | Standard request SOM=1 (44B)
Format | standard_request_som0.ksy | Standard request SOM=0 (16B)
Format | optimized_non_matching.ksy | Optimized non-matching (32B)
Format | small_message.ksy | Small message (32B)
Format | small_rma.ksy | Small RMA (32B)
Format | response.ksy | Response (16B)
Format | response_with_data.ksy | Response with data (24B)
Format | optimized_response_with_data.ksy | Optimized response (16B)
Format | rendezvous_extension.ksy | Rendezvous extension (32B)
Format | atomic_extension.ksy | Atomic extension (8B)
Format | cas_extension.ksy | CAS extension (40B)
Format | deferrable_send_request.ksy | Deferrable send (44B)
Format | ready_to_restart.ksy | Ready to restart (44B)
Format | opcodes.ksy | SES opcodes
Format | next_header_types.ksy | Next header types
Sequence | single_packet_request.ksy | Single packet request
Sequence | multi_packet_request.ksy | Multi packet request
Sequence | read_standard.ksy | Standard read

## Slide 96: transport/ses/ (27 files) (2/2)
Category | File | Description
Sequence | read_large_ack.ksy | Large read with ACK
Sequence | rendezvous_expected.ksy | Rendezvous expected
Sequence | rendezvous_unexpected.ksy | Rendezvous unexpected
Sequence | deferrable_expected.ksy | Deferrable expected
Sequence | deferrable_unexpected.ksy | Deferrable unexpected
Sequence | deferrable_no_buffer.ksy | Deferrable no buffer
Sequence | buffered_messages.ksy | Buffered messages
Sequence | buffered_headers.ksy | Buffered headers
Sequence | backoff_retry.ksy | Backoff retry

## Slide 97: transport/cms/ (15 files)
Category | File | Description
Format | ack_cc_state_nscc.ksy | NSCC CC state (8B)
Format | ack_cc_state_rccc_tfc.ksy | RCCC/TFC CC state (8B)
Format | req_cc_state.ksy | Request CC state (8B)
Format | credit_cp_payload.ksy | Credit CP payload
Format | credit_request_cp_payload.ksy | Credit request payload
Format | cc_type.ksy | CC type enum
Format | ccx_type.ksy | CCX type enum
Protocol | ccc_state_machine.ksy | CCC state machine
Protocol | nscc_source.ksy | NSCC source
Protocol | nscc_destination.ksy | NSCC destination
Protocol | rccc_source.ksy | RCCC source
Protocol | rccc_destination.ksy | RCCC destination
Protocol | tfc_source.ksy | TFC source
Protocol | tfc_destination.ksy | TFC destination
Protocol | multipath_selection.ksy | Multipath selection

## Slide 98: transport/tss/ (9 files)
Category | File | Description
Format | security_header.ksy | Security header (12-16B)
Format | iv_construction.ksy | IV construction (12B)
Protocol | tss_tx_processing.ksy | TX processing
Protocol | tss_rx_processing.ksy | RX processing
Protocol | key_rotation.ksy | Key rotation
Protocol | join_secure_domain.ksy | Join secure domain
Protocol | kdf_direct.ksy | KDF direct
Protocol | kdf_client_server.ksy | KDF client-server
Protocol | kdf_cluster.ksy | KDF cluster

## Slide 99: link/llr/ (9 files)
Category | File | Description
Format | llr_ack_ctlos.ksy | LLR_ACK CtlOS (8B)
Format | llr_nack_ctlos.ksy | LLR_NACK CtlOS (8B)
Format | llr_init_ctlos.ksy | LLR_INIT CtlOS (8B)
Format | llr_init_echo_ctlos.ksy | LLR_INIT_ECHO CtlOS (8B)
Format | llr_preamble_mii.ksy | LLR preamble MII (8B)
Format | llr_preamble_64b66b.ksy | LLR preamble 64B/66B (8B)
Protocol | llr_transmit_sm.ksy | LLR transmit SM
Protocol | llr_receive.ksy | LLR receive SM
Protocol | ack_nack_transmit_sm.ksy | ACK/NACK transmit SM

## Slide 100: link/cbfc/ (5 files)
Category | File | Description
Format | cf_update.ksy | CF_Update CtlOS (8B)
Format | cc_update.ksy | CC_Update message (8B)
Protocol | vc_state_machine.ksy | VC state machine
Protocol | lossless_vc_init.ksy | Lossless VC init
Protocol | lossless_vc_removal.ksy | Lossless VC removal

## Slide 101: link/lldp/ (3 files)
Category | File | Description
Format | ue_link_negotiation_tlv.ksy | Link negotiation TLV
Format | ue_cbfc_tlv.ksy | CBFC TLV
Protocol | link_negotiation_sm.ksy | Link negotiation SM

## Slide 102: network/ (4 files)
Category | File | Description
Format | dscp_categories.ksy | DSCP categories
Format | packet_trimming.ksy | Packet trimming
Format | ufh_16.ksy | UFH 16-bit
Format | ufh_32.ksy | UFH 32-bit

## Slide 103: physical/ (1 file)
Category | File | Description
Format | control_ordered_sets.ksy | Control Ordered Sets

## Slide 104: Detailed Header Formats
Field-level documentation with packet diagrams

## Slide 105: LLR Preamble 64B/66B Block Format
8 bytes (64 bits)

## Slide 106: llr_preamble_64b66b Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| sequence_number | control_flags|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| reserved |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 107: llr_preamble_64b66b Field Definitions
Field | Bits | Offset | Type | Description
sequence_number | 24 | 0 | b24 | Sequence number (24 bits). LLR frame sequence number.
control_flags | 8 | 24 | u1 | Control flags (8 bits). LLR-specific control.
reserved | 32 | 32 |  | Reserved (32 bits). MUST be 0.

## Slide 108: LLR_ACK Control Ordered Set (CtlOS)
8 bytes (64 bits)

## Slide 109: llr_ack_ctlos Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| block_type | ctlos_type |ack_nack_seq_hi|ack_nack_seq_m|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|ack_nack_seq_lo| reserved_d5 | reserved_d6 | reserved_d7 |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 110: llr_ack_ctlos Field Definitions
Field | Bits | Offset | Type | Description
block_type | 8 | 0 | u1 | Block Type Field for 64B/66B control block.
ctlos_type | 8 | 8 | u1 | CtlOS Message Type identifier.
ack_nack_seq_high | 8 | 16 | u1 | ACK/NACK sequence number bits [19:12] (upper 8 bits).
ack_nack_seq_mid | 8 | 24 | u1 | ACK/NACK sequence number bits [11:4] (middle 8 bits).
ack_nack_seq_low_and_ocode | 8 | 32 | u1 | Combined field containing:
reserved_d5 | 8 | 40 | u1 | Reserved field. MUST be 0x00.
reserved_d6 | 8 | 48 | u1 | Reserved field. MUST be 0x00.
reserved_d7 | 8 | 56 | u1 | Reserved field. MUST be 0x00.

## Slide 111: LLR_NACK Control Ordered Set (CtlOS)
8 bytes (64 bits)

## Slide 112: llr_nack_ctlos Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| block_type | ctlos_type |ack_nack_seq_hi|ack_nack_seq_m|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|ack_nack_seq_lo| reserved_d5 | reserved_d6 | reserved_d7 |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 113: llr_nack_ctlos Field Definitions
Field | Bits | Offset | Type | Description
block_type | 8 | 0 | u1 | Block Type Field for 64B/66B control block. MUST be 0x4B.
ctlos_type | 8 | 8 | u1 | CtlOS Message Type identifier. MUST be 0x02 for LLR_NACK.
ack_nack_seq_high | 8 | 16 | u1 | ACK/NACK sequence number bits [19:12] (upper 8 bits).
ack_nack_seq_mid | 8 | 24 | u1 | ACK/NACK sequence number bits [11:4] (middle 8 bits).
ack_nack_seq_low_and_ocode | 8 | 32 | u1 | Combined field: ack_nack_seq[3:0] (upper nibble) + O-code (l
reserved_d5 | 8 | 40 | u1 | Reserved field. MUST be 0x00.
reserved_d6 | 8 | 48 | u1 | Reserved field. MUST be 0x00.
reserved_d7 | 8 | 56 | u1 | Reserved field. MUST be 0x00.

## Slide 114: CBFC CF_Update Control Ordered Set (CtlOS)
8 bytes (64 bits)

## Slide 115: cbfc_cf_update Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| control_char | message_type |cf1_vc_and_coun| cf1_count_mid|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
|cf1_count_low_a|cf2_vc_and_coun| cf2_count_mid |cf2_count_low_|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 116: cbfc_cf_update Field Definitions
Field | Bits | Offset | Type | Description
control_char | 8 | 0 | u1 | Control character value for UE control ordered set.
message_type | 8 | 8 | u1 | CtlOS Message Type identifier.
cf1_vc_and_count_high | 8 | 16 | u1 | Combined field containing:
cf1_count_mid | 8 | 24 | u1 | CF1 credit count bits [10:3] (middle 8 bits of 15-bit count)
cf1_count_low_and_ocode | 8 | 32 | u1 | Combined field containing:
cf2_vc_and_count_high | 8 | 40 | u1 | Combined field containing:
cf2_count_mid | 8 | 48 | u1 | CF2 credit count bits [10:3] (middle 8 bits of 15-bit count)
cf2_count_low_and_reserved | 8 | 56 | u1 | Combined field containing:

## Slide 117: CBFC CC_Update Message
8 bytes (64 bits)

## Slide 118: cbfc_cc_update Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| message_type |vc_index_and_cc|cc_counter_mid |cc_counter_low|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| reserved |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 119: cbfc_cc_update Field Definitions
Field | Bits | Offset | Type | Description
message_type | 8 | 0 | u1 | Message type identifier for CC_Update.
vc_index_and_cc_high | 8 | 8 | u1 | Combined field:
cc_counter_mid | 8 | 16 | u1 | CC counter middle 8 bits.
cc_counter_low | 8 | 24 | u1 | CC counter lower 4 bits (upper nibble).
reserved | 32 | 32 |  | Reserved (32 bits). MUST be 0.

## Slide 120: UE Link Negotiation Options TLV
5 bytes (40 bits)

## Slide 121: ue_link_negotiation_tlv Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| tlv_type | tlv_length | subtype |l|c| reserved |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| ue_version |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 122: ue_link_negotiation_tlv Field Definitions
Field | Bits | Offset | Type | Description
tlv_type | 7 | 0 | b7 | TLV Type = 127 (Organizationally Specific TLV).
tlv_length | 9 | 7 | b9 | TLV Length in octets (variable, includes OUI + Subtype + Val
oui | 0 | 16 | u3 | Organizationally Unique Identifier (OUI) for Ultra Ethernet
subtype | 8 | 16 | u1 | UE-specific subtype = 1 (Link Negotiation Options).
llr_enabled | 1 | 24 | b1 | Link Layer Retry (LLR) enabled flag.
cbfc_enabled | 1 | 25 | b1 | Credit-Based Flow Control (CBFC) enabled flag.
reserved | 6 | 26 | b6 | Reserved bits, must be 0.
ue_version | 8 | 32 | u1 | UE Specification version supported.

## Slide 123: UE CBFC TLV
12 bytes (96 bits)

## Slide 124: ue_cbfc_tlv Packet Layout
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| tlv_type | tlv_length | subtype | num_vcs |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| credit_pool_size | lossless_vcs |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| lossless_vcs | reserved |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

## Slide 125: ue_cbfc_tlv Field Definitions
Field | Bits | Offset | Type | Description
tlv_type | 7 | 0 | b7 | TLV Type = 127 (Organizationally Specific TLV).
tlv_length | 9 | 7 | b9 | TLV Length in octets (variable, includes OUI + Subtype + Val
oui | 0 | 16 | u3 | Organizationally Unique Identifier (OUI) for Ultra Ethernet
subtype | 8 | 16 | u1 | UE-specific subtype = 2 (CBFC Configuration).
num_vcs | 8 | 24 | u1 | Number of virtual channels (VCs) supported.
credit_pool_size | 16 | 32 | u2 | Total credit pool size (in credits).
lossless_vcs | 32 | 48 | u4 | Bitmap of lossless VCs (bit N = 1 if VC N is lossless).
reserved | 16 | 80 | u2 | Reserved bytes, must be 0.

## Slide 126: References
Specification and Documentation Sources

## Slide 127: Primary References
• UE Specification v1.0.1, Chapter 3 (Transport Layer)
• UE Specification v1.0.1, Chapter 4 (Network Layer)
• UE Specification v1.0.1, Chapter 5 (Link Layer)
• UE Specification v1.0.1, Section 3.4 (SES)
• UE Specification v1.0.1, Section 3.5 (PDS)
• UE Specification v1.0.1, Section 3.6 (CMS)
• UE Specification v1.0.1, Section 3.7 (TSS)
• UE Specification v1.0.1, Section 5.1 (LLR)
• UE Specification v1.0.1, Section 5.2 (CBFC)
• IEEE 802.3-2022, Clause 82.2.3 (64B/66B Block Format)

## Slide 128: Analysis Documents
• analysis/packet_taxonomy/packet_taxonomy_ue_pds.md - PDS format details
• analysis/packet_taxonomy/packet_taxonomy_ue_ses.md - SES format details
• analysis/packet_taxonomy/packet_taxonomy_ue_cms_tss.md - CMS/TSS format details
• analysis/packet_taxonomy/packet_taxonomy_ue_link.md - Link layer format details

## Slide 129: Datamodel Location
• earlysim/datamodel/protocols/ue/transport/pds/ - 30 PDS files
• earlysim/datamodel/protocols/ue/transport/ses/ - 27 SES files
• earlysim/datamodel/protocols/ue/transport/cms/ - 15 CMS files
• earlysim/datamodel/protocols/ue/transport/tss/ - 9 TSS files
• earlysim/datamodel/protocols/ue/link/llr/ - 9 LLR files
• earlysim/datamodel/protocols/ue/link/cbfc/ - 5 CBFC files
• earlysim/datamodel/protocols/ue/link/lldp/ - 3 LLDP files
• earlysim/datamodel/protocols/ue/network/ - 4 network files
• earlysim/datamodel/protocols/ue/physical/ - 1 physical file